## Slide 1
What technology is used with half-duplex Ethernet networks?
A. CSMA/CA
B. CSMA/CD
C. CSMA/CC
D. CSMA/CQ

## Slide 2
What technology is used with half-duplex Ethernet networks?
A. CSMA/CA
B. CSMA/CD
C. CSMA/CC
D. CSMA/CQ

## Slide 3
What network infrastructure component is now frequently a replacement for router on a stick?
A. Access point
B. Endpoint
C. L2 switch
D. L3 switch

## Slide 4
What network infrastructure component is now frequently a replacement for router on a stick?
A. Access point
B. Endpoint
C. L2 switch
D. L3 switch

## Slide 5
What technology eliminates the major concerns about crossover versus
straight-through cables?
A. STP
B. RSTP
C. Auto MDI-X
D. FabricPath

## Slide 6
What technology eliminates the major concerns about crossover versus
straight-through cables?
A. STP
B. RSTP
C. Auto MDI-X
D. FabricPath

## Slide 7
What physical medium is used with 40GBASE-LR4?
A. Copper
B. Fiber
C. IR
D. Radio frequency/radio waves

## Slide 8
What physical medium is used with 40GBASE-LR4?
A. Copper
B. Fiber
C. IR
D. Radio frequency/radio waves

## Slide 9
Which of the following is not a valid error typically seen in show interface output?
A. Babble
B. Late collision
C. Ignored
D. Trickle

## Slide 10
Which of the following is not a valid error typically seen in show interface output?
A. Babble
B. Late collision
C. Ignored
D. Trickle

## Slide 11
What counter increments if the number of frames transmitted is greater than 1518
bytes in size?
A. Babble
B. Late collision
C. Runt
D. Ignored

## Slide 12
What counter increments if the number of frames transmitted is greater than 1518
bytes in size?
A. Babble
B. Late collision
C. Runt
D. Ignored

## Slide 13
What process on a Cisco device attempts to dynamically resolve speed and
duplex between two devices?
A. Negotiation
B. Autonegotiation
C. CDP
D. LLDP

## Slide 14
What process on a Cisco device attempts to dynamically resolve speed and
duplex between two devices?
A. Negotiation
B. Autonegotiation
C. CDP
D. LLDP

## Slide 15
1. What is the physical medium used by 802.3an?
A. Copper
B. Multimode fiber
C. Single-mode fiber
D. Wireless

## Slide 16
1. What is the physical medium used by 802.3an?
A. Copper
B. Multimode fiber
C. Single-mode fiber
D. Wireless

## Slide 17
If you are not using Auto MDI-X on a Cisco switch, what type of cable is used to
connect a Layer 2 switch’s port to a PC?
A. Crossover
B. Rollover
C. Console
D. Straight-through

## Slide 18
If you are not using Auto MDI-X on a Cisco switch, what type of cable is used to
connect a Layer 2 switch’s port to a PC?
A. Crossover
B. Rollover
C. Console
D. Straight-through

## Slide 19
What is the duplex setting used throughout a point-to-point Ethernet network?
A. Half-duplex
B. Full-duplex
C. Main duplex
D. Dual-duplex

## Slide 20
What is the duplex setting used throughout a point-to-point Ethernet network?
A. Half-duplex
B. Full-duplex
C. Main duplex
D. Dual-duplex

## Slide 21
What was the original PoE standard designation?
A. 802.3bt
B. 802.3at
C. 802.3af
D. 802.3bu

## Slide 22
What was the original PoE standard designation?
A. 802.3bt
B. 802.3at
C. 802.3af
D. 802.3bu

## Slide 23
What type of cable is used to connect a switch to another switch?
A. Straight-through
B. Crossover
C. Null
D. Dual-band

## Slide 24
What type of cable is used to connect a switch to another switch?
A. Straight-through
B. Crossover
C. Null
D. Dual-band

## Slide 25
You are analyzing the frames sent and received over a Gigabit Ethernet connection, and you are surprised to see many frames that are approximately 9000 bytes in size. What is the term for these frames?
A. Error frames
B. Pico frames
C. Runts
D. Jumbo frames

## Slide 26
You are analyzing the frames sent and received over a Gigabit Ethernet connection, and you are surprised to see many frames that are approximately 9000 bytes in size. What is the term for these frames?
A. Error frames
B. Pico frames
C. Runts
D. Jumbo frames

## Slide 27
What protocol does a host use to discover the L2 address of the next device in
the path toward a remote destination?
A. TCP
B. UDP
C. ICMP
D. ARP

## Slide 28
What protocol does a host use to discover the L2 address of the next device in
the path toward a remote destination?
A. TCP
B. UDP
C. ICMP
D. ARP

## Slide 29
2. What layer of the OSI model corresponds to the transport layer of the TCP/IP
model?
A. Network
B. Transport
C. Session
D. Presentation

## Slide 30
2. What layer of the OSI model corresponds to the transport layer of the TCP/IP
model?
A. Network
B. Transport
C. Session
D. Presentation

## Slide 31
What port number does SNMP use, and what protocol does it use? (Choose two.)
A. TCP
B. UDP
C. 161
D. 514

## Slide 32
What port number does SNMP use, and what protocol does it use? (Choose two.)
A. TCP
B. UDP
C. 161
D. 514

## Slide 33
What layer of the OSI model exists just above the network layer?
A. Session
B. Presentation
C. Application
D. Transport

## Slide 34
What layer of the OSI model exists just above the network layer?
A. Session
B. Presentation
C. Application
D. Transport

## Slide 35
What form of flow control is used with TCP?
A. None
B. Random
C. Windowing
D. Explicit buffering

## Slide 36
What form of flow control is used with TCP?
A. None
B. Random
C. Windowing
D. Explicit buffering

## Slide 37
What are the terms for the four PDUs that exist at the bottom of the OSI model?
Name them in order, from bottom to top.
A. Segments, frames, packets, bits
B. Bits, frames, packets, segments
C. Packets, frames, bits, segments
D. Segments, packets, frames, bits

## Slide 38
What are the terms for the four PDUs that exist at the bottom of the OSI model?
Name them in order, from bottom to top.
A. Segments, frames, packets, bits
B. Bits, frames, packets, segments
C. Packets, frames, bits, segments
D. Segments, packets, frames, bits

## Slide 39
Which of the following are transport layer protocols? (Choose two.)
A. ICMP
B. TCP
C. UDP
D. FTP

## Slide 40
Which of the following are transport layer protocols? (Choose two.)
A. ICMP
B. TCP
C. UDP
D. FTP

## Slide 41
What protocol uses windowing to implement flow control?
A. ICMP
B. TCP
C. UDP
D. RIP

## Slide 42
What protocol uses windowing to implement flow control?
A. ICMP
B. TCP
C. UDP
D. RIP

## Slide 43
What port number does SSH use, and what protocol does it use? (Choose two.)
A. TCP
B. UDP
C. 22
D. 23

## Slide 44
What port number does SSH use, and what protocol does it use? (Choose two.)
A. TCP
B. UDP
C. 22
D. 23

## Slide 45
What is 203 converted to binary?
A. 11001011
B. 11101011
C. 10101100
D. 11001000

## Slide 46
What is 203 converted to binary?
A. 11001011
B. 11101011
C. 10101100
D. 11001000

## Slide 47
What is 01101111 in decimal?
A. 112
B. 111
C. 120
D. 110

## Slide 48
What is 01101111 in decimal?
A. 112
B. 111
C. 120
D. 110

## Slide 49
What is the default subnet mask for a class B network?
A. 255.255.255.0
B. 255.0.0.0
C. 255.255.0.0
D. 255.255.255.255

## Slide 50
What is the default subnet mask for a class B network?
A. 255.255.255.0
B. 255.0.0.0
C. 255.255.0.0
D. 255.255.255.255

## Slide 51
If a subnet mask has a length of 19 bits, what is the subnet mask in dotted decimal notation?
A. 255.255.192.0
B. 255.255.224.0
C. 255.255.240.0
D. 255.255.252.0

## Slide 52
If a subnet mask has a length of 19 bits, what is the subnet mask in dotted decimal notation?
A. 255.255.192.0
B. 255.255.224.0
C. 255.255.240.0
D. 255.255.252.0

## Slide 53
If you have the mask 255.255.255.240, how many hosts can you support?
A. 32
B. 62
C. 14
D. 6

## Slide 54
If you have the mask 255.255.255.240, how many hosts can you support?
A. 32
B. 62
C. 14
D. 6

## Slide 55
Your network needs to support 30 subnets. How many bits should you “borrow” from the host portion of the address in order to create the least waste in terms of address space?
A. 4
B. 5
C. 6
D. 7

## Slide 56
Your network needs to support 30 subnets. How many bits should you “borrow” from the host portion of the address in order to create the least waste in terms of address space?
A. 4
B. 5
C. 6
D. 7

## Slide 57
What is the last usable host address on a subnet where a host has been given the
address 172.16.7.1 255.255.254.0?
A. 172.16.7.255
B. 172.16.6.1
C. 172.16.7.128
D. 172.16.7.254

## Slide 58
What is the last usable host address on a subnet where a host has been given the
address 172.16.7.1 255.255.254.0?
A. 172.16.7.255
B. 172.16.6.1
C. 172.16.7.128
D. 172.16.7.254

## Slide 59
What type of IP traffic is used when communicating directly between two nodes
(for example, in exchanging email)?
A. Broadcast
B. Multicast
C. Unicast
D. Anycast

## Slide 60
What type of IP traffic is used when communicating directly between two nodes
(for example, in exchanging email)?
A. Broadcast
B. Multicast
C. Unicast
D. Anycast

## Slide 61
EIGRP uses the IPv4 address 224.0.0.10 in its operation. What type of address
is this?
A. Unicast
B. Broadcast
C. Multicast
D. Anycast

## Slide 62
EIGRP uses the IPv4 address 224.0.0.10 in its operation. What type of address
is this?
A. Unicast
B. Broadcast
C. Multicast
D. Anycast

## Slide 63
What does it mean when you see FF:FF:FF:FF:FF:FF as the destination address in an Ethernet frame?
A. It means the frame is a multicast frame.
B. It means the frame is a unicast frame.
C. It means the frame should be dropped.
D. It means the frame is a broadcast frame.

## Slide 64
What does it mean when you see FF:FF:FF:FF:FF:FF as the destination address in an Ethernet frame?
A. It means the frame is a multicast frame.
B. It means the frame is a unicast frame.
C. It means the frame should be dropped.
D. It means the frame is a broadcast frame.

## Slide 65
Which of the following is not a private address?
A. 10.10.10.1
B. 12.34.100.1
C. 172.16.1.10
D. 192.168.1.10

## Slide 66
Which of the following is not a private address?
A. 10.10.10.1
B. 12.34.100.1
C. 172.16.1.10
D. 192.168.1.10

## Slide 67
What famous RFC defines what IP address space is for private use only?
A. RFC 2020
B. RFC 2191
C. RFC 2001
D. RFC 1918

## Slide 68
What famous RFC defines what IP address space is for private use only?
A. RFC 2020
B. RFC 2191
C. RFC 2001
D. RFC 1918

## Slide 69
What is 2 raised to the 7th power?
A. 64
B. 128
C. 32
D. 16

## Slide 70
What is 2 raised to the 7th power?
A. 64
B. 128
C. 32
D. 16

## Slide 71
Which of the following is true of the IP address 127.0.0.1?
A. This is a multicast address.
B. This is a Class A unicast address.
C. This is a loopback address.
D. This is an invalid IP address.

## Slide 72
Which of the following is true of the IP address 127.0.0.1?
A. This is a multicast address.
B. This is a Class A unicast address.
C. This is a loopback address.
D. This is an invalid IP address.

## Slide 73
What is the subnet mask if you begin with the default Class A mask and then
“borrow” 4 bits for subnetting?
A. 255.255.128.0
B. 255.255.240.0
C. 255.240.0.0
D. 255.255.255.240

## Slide 74
What is the subnet mask if you begin with the default Class A mask and then
“borrow” 4 bits for subnetting?
A. 255.255.128.0
B. 255.255.240.0
C. 255.240.0.0
D. 255.255.255.240

## Slide 75
If you need to create six subnets and want to waste as little IP address space as
possible, how many bits should you “borrow”?
A. 2
B. 3
C. 4
D. 5

## Slide 76
If you need to create six subnets and want to waste as little IP address space as
possible, how many bits should you “borrow”?
A. 2
B. 3
C. 4
D. 5

## Slide 77
What is the Layer 3 broadcast address?
A. 127.255.255.255
B. 0.0.0.0
C. 1.1.1.1
D. 255.255.255.255

## Slide 78
What is the Layer 3 broadcast address?
A. 127.255.255.255
B. 0.0.0.0
C. 1.1.1.1
D. 255.255.255.255

## Slide 79
What is the range of Class B private addresses?
A. 172.16.0.0 to 172.16.255.255
B. 172.0.0.0 to 172.255.255.255
C. 172.16.0.0 to 172.31.255.255
D. 172.32.0.0 to 172.36.255.255

## Slide 80
What is the range of Class B private addresses?
A. 172.16.0.0 to 172.16.255.255
B. 172.0.0.0 to 172.255.255.255
C. 172.16.0.0 to 172.31.255.255
D. 172.32.0.0 to 172.36.255.255

## Slide 81
What parameters is your engineer most likely verifying when she enters ifconfig on your Linux system?
A. Duration of the current interface state
B. OS version information
C. Registry settings
D. IP address settings

## Slide 82
What parameters is your engineer most likely verifying when she enters ifconfig on your Linux system?
A. Duration of the current interface state
B. OS version information
C. Registry settings
D. IP address settings

## Slide 83
What is the size of the source address field in an IPv6 header?
A. 6 bytes
B. 8 bytes
C. 12 bytes
D. 16 bytes

## Slide 84
What is the size of the source address field in an IPv6 header?
A. 6 bytes
B. 8 bytes
C. 12 bytes
D. 16 bytes

## Slide 85
What are two rules you can use to shorten an IPv6 address? (Choose two.)
A. You can trim all trailing zeros in all sections.
B. You can trim all leading zeros in all sections.
C. You can use :: twice in an address.
D. You can use :: once in an address.

## Slide 86
What are two rules you can use to shorten an IPv6 address? (Choose two.)
A. You can trim all trailing zeros in all sections.
B. You can trim all leading zeros in all sections.
C. You can use :: twice in an address.
D. You can use :: once in an address.

## Slide 87
How large is the typical network portion of an IPv6 global unicast address?
A. 32 bits
B. 48 bits
C. 64 bits
D. 128 bits

## Slide 88
How large is the typical network portion of an IPv6 global unicast address?
A. 32 bits
B. 48 bits
C. 64 bits
D. 128 bits

## Slide 89
What does a link-local address begin with?
A. FD80::/10
B. FE80::/10
C. FF80::/10
D. FC80::/10

## Slide 90
What does a link-local address begin with?
A. FD80::/10
B. FE80::/10
C. FF80::/10
D. FC80::/10

## Slide 91
What address does IPv6 use in order to multicast traffic to all devices on a network segment?
A. FF02::1
B. FF02::2
C. FF02::5
D. FF02::6

## Slide 92
What address does IPv6 use in order to multicast traffic to all devices on a network segment?
A. FF02::1
B. FF02::2
C. FF02::5
D. FF02::6

## Slide 93
When troubleshooting an IPv6 network, you notice that two devices have identical
IPv6 addresses. If the network is actually configured correctly, why might this occur?
A. The devices are using broadcasts for routing protocol traffic.
B. The devices are using anycast.
C. The devices are using matching link-local addresses for the purpose of SLAAC.
D. The devices are using unique local addresses.

## Slide 94
When troubleshooting an IPv6 network, you notice that two devices have identical
IPv6 addresses. If the network is actually configured correctly, why might this occur?
A. The devices are using broadcasts for routing protocol traffic.
B. The devices are using anycast.
C. The devices are using matching link-local addresses for the purpose of SLAAC.
D. The devices are using unique local addresses.

## Slide 95
What command do you use to enable IPv6 routing capabilities on a Cisco router?
A. ipv6 unicast-routing
B. ipv6 routing
C. ipv6 routing enable
D. ipv6 unicast-enable

## Slide 96
What command do you use to enable IPv6 routing capabilities on a Cisco router?
A. ipv6 unicast-routing
B. ipv6 routing
C. ipv6 routing enable
D. ipv6 unicast-enable

## Slide 97
What command configures IPv6 on an interface and eliminates the need to manually
configure the host portion of the address?
A. ipv6 address 2001:aaaa:bbbb::/64 auto
B. ipv6 address 2001:aaaa:bbbb::/64
C. ipv6 address 2001:aaaa:bbbb::/64 eui-64
D. ipv6 address 2001:aaaa:bbbb::/64 slaac

## Slide 98
What command configures IPv6 on an interface and eliminates the need to manually
configure the host portion of the address?
A. ipv6 address 2001:aaaa:bbbb::/64 auto
B. ipv6 address 2001:aaaa:bbbb::/64
C. ipv6 address 2001:aaaa:bbbb::/64 eui-64
D. ipv6 address 2001:aaaa:bbbb::/64 slaac

## Slide 99
Which commands could you use to verify your IPv6 interface address?
(Choose two.)
A. show ipv6 interface brief
B. show interface ipv6 details
C. show ipv6 interface
D. show interface ipv6 info

## Slide 100
Which commands could you use to verify your IPv6 interface address?
(Choose two.)
A. show ipv6 interface brief
B. show interface ipv6 details
C. show ipv6 interface
D. show interface ipv6 info

## Slide 101
You run ipconfig on your Windows system and see an IPv6 address that starts FE80. What type of address is this?
A. Global unicast
B. Multicast
C. Anycast
D. Link local

## Slide 102
You run ipconfig on your Windows system and see an IPv6 address that starts FE80. What type of address is this?
A. Global unicast
B. Multicast
C. Anycast
D. Link local

## Slide 103
What ipconfig switch ensures that you can see the IPv6 parameters of your
interface?
A. /verbose
B. /ipv6
C. /all
D. /new

## Slide 104
What ipconfig switch ensures that you can see the IPv6 parameters of your
interface?
A. /verbose
B. /ipv6
C. /all
D. /new

## Slide 105
How many more bits are used in an IPv6 address than in an IPv4 address?
A. 96
B. 128
C. 48
D. 64

## Slide 106
How many more bits are used in an IPv6 address than in an IPv4 address?
A. 96
B. 128
C. 48
D. 64

## Slide 107
What is the significance of :: in the IPv6 address 2001:0:11:1::1:1AB1/64?
A. It is used to represent a single section of 0000.
B. It is used to represent consecutive sections of 0000.
C. It is used to represent a single section of 1111.
D. It is used to represent consecutive sections of 1111

## Slide 108
What is the significance of :: in the IPv6 address 2001:0:11:1::1:1AB1/64?
A. It is used to represent a single section of 0000.
B. It is used to represent consecutive sections of 0000.
C. It is used to represent a single section of 1111.
D. It is used to represent consecutive sections of 1111

## Slide 109
What command causes a router interface to autoconfigure its host portion of the address?
A. ipv6 address 2001:aaaa:bbbb::1/64 auto
B. ipv6 address 2001:aaaa:bbbb::1/64 eui-64
C. ipv6 address 2001:aaaa:bbbb::/64 eui-64
D. ipv6 address 2001:aaaa:bbbb::/64 auto

## Slide 110
What command causes a router interface to autoconfigure its host portion of the address?
A. ipv6 address 2001:aaaa:bbbb::1/64 auto
B. ipv6 address 2001:aaaa:bbbb::1/64 eui-64
C. ipv6 address 2001:aaaa:bbbb::/64 eui-64
D. ipv6 address 2001:aaaa:bbbb::/64 auto

## Slide 111
What command allows you to see the multicast addresses that an interface has
joined in IPv6?
A. show ipv6 interface brief
B. show ipv6 interface
C. show ipv6 interface multicast
D. show multicast ipv6

## Slide 112
What command allows you to see the multicast addresses that an interface has
joined in IPv6?
A. show ipv6 interface brief
B. show ipv6 interface
C. show ipv6 interface multicast
D. show multicast ipv6

## Slide 113
If you are using DHCP combined with the SLAAC feature in IPv6, you are most likely using what form of DHCP?
A. Stateful
B. Stateless
C. Headless
D. Auto

## Slide 114
If you are using DHCP combined with the SLAAC feature in IPv6, you are most likely using what form of DHCP?
A. Stateful
B. Stateless
C. Headless
D. Auto

## Slide 115
If you use the ipv6 enable command on an interface, what address do you have on that interface?
A. Global unicast
B. Autoconfiguration
C. Unique local
D. Link local

## Slide 116
If you use the ipv6 enable command on an interface, what address do you have on that interface?
A. Global unicast
B. Autoconfiguration
C. Unique local
D. Link local

## Slide 117
When a frame enters a Cisco switch, what field does the switch learn from?
A. Preamble
B. FCS
C. Source MAC
D. Destination MAC

## Slide 118
When a frame enters a Cisco switch, what field does the switch learn from?
A. Preamble
B. FCS
C. Source MAC
D. Destination MAC

## Slide 119
What is the name of the database that stores address information in a Cisco
switch?
A. MAC address table
B. Routing table
C. Interface table
D. Buffer table

## Slide 120
What is the name of the database that stores address information in a Cisco
switch?
A. MAC address table
B. Routing table
C. Interface table
D. Buffer table

## Slide 121
What command allows you to view the addresses learned by a Cisco switch?
A. show mac-address-table
B. show mac address-table
C. show addresses
D. show mac addresses

## Slide 122
What command allows you to view the addresses learned by a Cisco switch?
A. show mac-address-table
B. show mac address-table
C. show addresses
D. show mac addresses

## Slide 123
Why might padding be used in an Ethernet frame?
A. To bring the entire length of the frame to 1500 bytes
B. To bring the length of the Data field to 46 bytes
C. To bring the length of the FCS field to 64 bytes
D. To bring the length of the SFD field to 1 byte

## Slide 124
Why might padding be used in an Ethernet frame?
A. To bring the entire length of the frame to 1500 bytes
B. To bring the length of the Data field to 46 bytes
C. To bring the length of the FCS field to 64 bytes
D. To bring the length of the SFD field to 1 byte

## Slide 125
If a switch has five workstations attached, how many collision domains are
created?
A. 1
B. 0
C. 5
D. 6

## Slide 126
If a switch has five workstations attached, how many collision domains are
created?
A. 1
B. 0
C. 5
D. 6

## Slide 127
Your 48-port Cisco switch has been configured with five different VLANs. How
many broadcast domains exist on the switch?
A. 0
B. 1
C. 5
D. 48

## Slide 128
Your 48-port Cisco switch has been configured with five different VLANs. How
many broadcast domains exist on the switch?
A. 0
B. 1
C. 5
D. 48

## Slide 129
What command allows you to view the VLANs and interface assignments on a
switch?
A. show vlan brief
B. show vlan status
C. show vlan summary
D. show vlan database

## Slide 130
What command allows you to view the VLANs and interface assignments on a
switch?
A. show vlan brief
B. show vlan status
C. show vlan summary
D. show vlan database

## Slide 131
What command assigns an access port to VLAN 20?
A. switchport vlan 20
B. switchport mode vlan 20
C. switchport assign vlan 20
D. switchport access vlan 20

## Slide 132
What command assigns an access port to VLAN 20?
A. switchport vlan 20
B. switchport mode vlan 20
C. switchport assign vlan 20
D. switchport access vlan 20

## Slide 133
What command assigns voice VLAN 10 on a switch access port?
A. switchport voice vlan 10
B. switchport access vlan 10 voice
C. switchport vlan 10 voice
D. switchport access vlan 10

## Slide 134
What command assigns voice VLAN 10 on a switch access port?
A. switchport voice vlan 10
B. switchport access vlan 10 voice
C. switchport vlan 10 voice
D. switchport access vlan 10

## Slide 135
What command allows you to verify the voice VLAN configuration?
A. show interface gi0/1 voice
B. show interface gi0/1 switchport
C. show interface gi0/1 vlan
D. show interface gi0/1 vlan assign

## Slide 136
What command allows you to verify the voice VLAN configuration?
A. show interface gi0/1 voice
B. show interface gi0/1 switchport
C. show interface gi0/1 vlan
D. show interface gi0/1 vlan assign

## Slide 137
Where is an 802.1Q tag inserted in a frame?
A. Between the Preamble and SFD fields
B. Between the Source and Destination MAC fields
C. Between the Source MAC and Type fields
D. Between the Source MAC and FCS fields

## Slide 138
Where is an 802.1Q tag inserted in a frame?
A. Between the Preamble and SFD fields
B. Between the Source and Destination MAC fields
C. Between the Source MAC and Type fields
D. Between the Source MAC and FCS fields

## Slide 139
What command configures an interface to trunk?
A. switchport trunk
B. switchport trunk dot1q
C. switchport mode trunk
D. switchport trunk enable

## Slide 140
What command configures an interface to trunk?
A. switchport trunk
B. switchport trunk dot1q
C. switchport mode trunk
D. switchport trunk enable

## Slide 141
What command allows you to quickly view all the trunks on a switch?
A. show vlans trunk
B. show interface trunk
C. show trunk interface
D. show trunk all

## Slide 142
What command allows you to quickly view all the trunks on a switch?
A. show vlans trunk
B. show interface trunk
C. show trunk interface
D. show trunk all

## Slide 143
What is the default VLAN in Cisco networking?
A. VLAN 10
B. VLAN 0
C. VLAN 4092
D. VLAN 1

## Slide 144
What is the default VLAN in Cisco networking?
A. VLAN 10
B. VLAN 0
C. VLAN 4092
D. VLAN 1

## Slide 145
What command disables CDP globally on a device?
A. no cdp run
B. no cdp enable
C. cdp disable
D. cdp stop

## Slide 146
What command disables CDP globally on a device?
A. no cdp run
B. no cdp enable
C. cdp disable
D. cdp stop

## Slide 147
What command ensures that CDP is running on a specific interface?
A. cdp enable
B. cdp on
C. cdp run
D. cdp accept

## Slide 148
What command ensures that CDP is running on a specific interface?
A. cdp enable
B. cdp on
C. cdp run
D. cdp accept

## Slide 149
Which statement about CDP is correct?
A. CDP relies on TCP.
B. CDP is disabled by default.
C. CDP is disabled on all serial interfaces by default.
D. CDP is a Layer 2 protocol.

## Slide 150
Which statement about CDP is correct?
A. CDP relies on TCP.
B. CDP is disabled by default.
C. CDP is disabled on all serial interfaces by default.
D. CDP is a Layer 2 protocol.

## Slide 151
On a Cisco device, what command would you use on an interface to ensure that
the interface is sending LLDP frames?
A. lldp run
B. lldp forward
C. lldp transmit
D. lldp send

## Slide 152
On a Cisco device, what command would you use on an interface to ensure that
the interface is sending LLDP frames?
A. lldp run
B. lldp forward
C. lldp transmit
D. lldp send

## Slide 153
If a router cannot find a better match, what might the router use to route traffic?
A. 255.255.255.255/0
B. 127.0.0.1/32
C. 0.0.0.0/32
D. 0.0.0.0/0

## Slide 154
If a router cannot find a better match, what might the router use to route traffic?
A. 255.255.255.255/0
B. 127.0.0.1/32
C. 0.0.0.0/32
D. 0.0.0.0/0

## Slide 155
When a router forwards packets onto Ethernet, what is rewritten?
A. The source and destination IP addresses
B. Only the source IP address
C. Only the source MAC address
D. The source and destination MAC addresses

## Slide 156
When a router forwards packets onto Ethernet, what is rewritten?
A. The source and destination IP addresses
B. Only the source IP address
C. Only the source MAC address
D. The source and destination MAC addresses

## Slide 157
What does the routing protocol code B indicate in the routing table?
A. EIGRP
B. IGRP
C. RIP
D. OSPF
E. BGP

## Slide 158
What does the routing protocol code B indicate in the routing table?
A. EIGRP
B. IGRP
C. RIP
D. OSPF
E. BGP

## Slide 159
What is the administrative distance of Internal EIGRP routes?
A. 5
B. 20
C. 90
D. 100

## Slide 160
What is the administrative distance of Internal EIGRP routes?
A. 5
B. 20
C. 90
D. 100

## Slide 161
What is the unreachable AD?
A. 0
B. 100
C. 200
D. 255

## Slide 162
What is the unreachable AD?
A. 0
B. 100
C. 200
D. 255

## Slide 163
What is the mask length for a host route?
A. 0
B. 64
C. 16
D. 32

## Slide 164
What is the mask length for a host route?
A. 0
B. 64
C. 16
D. 32

## Slide 165
What command permits you to view the IPv6 routing table?
A. show route ipv6
B. show route new
C. show ipv6 route
D. show route

## Slide 166
What command permits you to view the IPv6 routing table?
A. show route ipv6
B. show route new
C. show ipv6 route
D. show route

## Slide 167
What type of static route is shown in the following example?
ip route 172.16.1.0 255.255.255.0 192.168.2.100
A. A static host route
B. A floating static route
C. A default route
D. A network static route

## Slide 168
What type of static route is shown in the following example?
ip route 172.16.1.0 255.255.255.0 192.168.2.100
A. A static host route
B. A floating static route
C. A default route
D. A network static route

## Slide 169
What is the default administrative distance of a static route that references a next
hop IP address?
A. 0
B. 1
C. 2
D. 10

## Slide 170
What is the default administrative distance of a static route that references a next
hop IP address?
A. 0
B. 1
C. 2
D. 10

## Slide 171
Which of the following routing protocols is considered to use link-state logic?
RIPv1
b. RIPv2
c. EIGRP
d. OSPF

## Slide 172
Which of the following routing protocols is considered to use link-state logic?
RIPv1
b. RIPv2
c. EIGRP
d. OSPF

## Slide 173
Which of the following routing protocols use a metric that is, by default, at least partially affected by link bandwidth? (Choose two answers.)
RIPv1
RIPv2
EIGRP
OSPF

## Slide 174
Which of the following routing protocols use a metric that is, by default, at least partially affected by link bandwidth? (Choose two answers.)
RIPv1
RIPv2
EIGRP
OSPF

## Slide 175
Which of the following interior routing protocols support VLSM? (Choose three answers.)
RIPv1
RIPv2
EIGRP
OSPF

## Slide 176
Which of the following interior routing protocols support VLSM? (Choose three answers.)
RIPv1
RIPv2
EIGRP
OSPF

## Slide 177
Two routers using OSPFv2 have become neighbors and exchanged all LSAs. As a result, Router R1 now lists some OSPF-learned routes in its routing table. Which of the following best describes how R1 uses those recently learned LSAs to choose which IP routes to add to its IP routing table?
Each LSA lists a route to be copied to the routing table.
Some LSAs list a route that can be copied to the routing table.
Run some SPF math against the LSAs to calculate the routes.
R1 does not use the LSAs at all when choosing what routes to add.

## Slide 178
Two routers using OSPFv2 have become neighbors and exchanged all LSAs. As a result, Router R1 now lists some OSPF-learned routes in its routing table. Which of the following best describes how R1 uses those recently learned LSAs to choose which IP routes to add to its IP routing table?
Each LSA lists a route to be copied to the routing table.
Some LSAs list a route that can be copied to the routing table.
Run some SPF math against the LSAs to calculate the routes.
R1 does not use the LSAs at all when choosing what routes to add.

## Slide 179
Which of the following OSPF neighbor states is expected when the exchange of topology information is complete between two OSPF neighbors?
2-way
Full
Up/up
Final

## Slide 180
Which of the following OSPF neighbor states is expected when the exchange of topology information is complete between two OSPF neighbors?
2-way
Full
Up/up
Final

## Slide 181
A company has a small/medium-sized network with 15 routers and 40 subnets and uses OSPFv2. Which of the following is considered an advantage of using a single-area design as opposed to a multiarea design?
It reduces the processing overhead on most routers.
Status changes to one link may not require SPF to run on all other routers.
It allows for simpler planning and operations.
It allows for route summarization, reducing the size of IP routing tables

## Slide 182
A company has a small/medium-sized network with 15 routers and 40 subnets and uses OSPFv2. Which of the following is considered an advantage of using a single-area design as opposed to a multiarea design?
It reduces the processing overhead on most routers.
Status changes to one link may not require SPF to run on all other routers.
It allows for simpler planning and operations.
It allows for route summarization, reducing the size of IP routing tables

## Slide 183
Which of the following commands list the OSPF neighbors off interface serial 0/0? (Choose two answers.)
show ip ospf neighbor
show ip ospf interface brief
show ip neighbor
show ip interface
show ip ospf neighbor serial 0/0

## Slide 184
Which of the following commands list the OSPF neighbors off interface serial 0/0? (Choose two answers.)
show ip ospf neighbor
show ip ospf interface brief
show ip neighbor
show ip interface
show ip ospf neighbor serial 0/0

## Slide 185
OSPF interface configuration uses the ip ospf process-id area area-number configuration command. In which modes do you configure the following settings when using this command?
The router ID is configured explicitly in router mode.
The router ID is configured explicitly in interface mode.
An interface’s area number is configured in router mode.
An interface’s area number is configured in interface mode

## Slide 186
OSPF interface configuration uses the ip ospf process-id area area-number configuration command. In which modes do you configure the following settings when using this command?
The router ID is configured explicitly in router mode.
The router ID is configured explicitly in interface mode.
An interface’s area number is configured in router mode.
An interface’s area number is configured in interface mode

## Slide 187
Routers R1 and R2, with router IDs 1.1.1.1 and 2.2.2.2, connect over an Ethernet WAN link. If using all default OSPF settings, if the WAN link initializes for both routers at the same time, which of the following answers are true? (Choose two answers.)
Router R1 will become the DR.
Router R1 will dynamically discover the existence of router R2.
Router R2 will be neither the DR nor the BDR.
Router R1’s show ip ospf neighbor command will list R2 with a state of “FULL/DR.”

## Slide 188
Routers R1 and R2, with router IDs 1.1.1.1 and 2.2.2.2, connect over an Ethernet WAN link. If using all default OSPF settings, if the WAN link initializes for both routers at the same time, which of the following answers are true? (Choose two answers.)
Router R1 will become the DR.
Router R1 will dynamically discover the existence of router R2.
Router R2 will be neither the DR nor the BDR.
Router R1’s show ip ospf neighbor command will list R2 with a state of “FULL/DR.”

## Slide 189
Routers R1 and R2, with router IDs 1.1.1.1 and 2.2.2.2, connect over an Ethernet WAN link. The configuration uses all defaults, except giving R1 an interface priority of 11 and changing both routers to use OSPF network type point-to-point. If the WAN link initializes for both routers at the same time, which of the following answers are true? (Choose two answers.)
Router R1 will become the DR.
Router R1 will dynamically discover the existence of router R2.
Router R2 will be neither the DR nor the BDR.
Router R2’s show ip ospf neighbor command will list R1 with a state of “FULL/DR.”

## Slide 190
Routers R1 and R2, with router IDs 1.1.1.1 and 2.2.2.2, connect over an Ethernet WAN link. The configuration uses all defaults, except giving R1 an interface priority of 11 and changing both routers to use OSPF network type point-to-point. If the WAN link initializes for both routers at the same time, which of the following answers are true? (Choose two answers.)
Router R1 will become the DR.
Router R1 will dynamically discover the existence of router R2.
Router R2 will be neither the DR nor the BDR.
Router R2’s show ip ospf neighbor command will list R1 with a state of “FULL/DR.”

## Slide 191
Per the command output, with how many routers is router R9 full adjacent over its Gi0/0 interface?
R9# show ip ospf interface brief
Interface PID Area IP Address/Mask Cost State Nbrs F/C
Gi0/0 1 0 10.1.1.1/24 1 DROTH 2/5
7
0
5
2

## Slide 192
Per the command output, with how many routers is router R9 full adjacent over its Gi0/0 interface?
R9# show ip ospf interface brief
Interface PID Area IP Address/Mask Cost State Nbrs F/C
Gi0/0 1 0 10.1.1.1/24 1 DROTH 2/5
7
0
5
2

## Slide 193
An engineer connects routers R11 and R12 to the same Ethernet LAN and configures them to use OSPFv2. Which answers describe a combination of settings that would prevent the two routers from becoming OSPF neighbors? (Choose two answers.)
R11’s interface uses area 11 while R12’s interface uses area 12.
R11’s OSPF process uses process ID 11 while R12 uses process ID 12.
R11’s interface uses OSPF priority 11 while R12’s uses OSPF priority 12.
R11’s interface uses an OSPF Hello timer value of 11 while R12’s uses 12.

## Slide 194
An engineer connects routers R11 and R12 to the same Ethernet LAN and configures them to use OSPFv2. Which answers describe a combination of settings that would prevent the two routers from becoming OSPF neighbors? (Choose two answers.)
R11’s interface uses area 11 while R12’s interface uses area 12.
R11’s OSPF process uses process ID 11 while R12 uses process ID 12.
R11’s interface uses OSPF priority 11 while R12’s uses OSPF priority 12.
R11’s interface uses an OSPF Hello timer value of 11 while R12’s uses 12.

## Slide 195
An engineer connects routers R13 and R14 to the same Ethernet LAN and configures them to use OSPFv2. Which answers describe a combination of settings that would prevent the two routers from becoming OSPF neighbors?
Both routers’ interface IP addresses reside in the same subnet.
Both routers’ OSPF process uses process ID 13.
Both routers’ OSPF process uses router ID 13.13.13.13.
Both routers’ interfaces use an OSPF Dead interval of 40.

## Slide 196
An engineer connects routers R13 and R14 to the same Ethernet LAN and configures them to use OSPFv2. Which answers describe a combination of settings that would prevent the two routers from becoming OSPF neighbors?
Both routers’ interface IP addresses reside in the same subnet.
Both routers’ OSPF process uses process ID 13.
Both routers’ OSPF process uses router ID 13.13.13.13.
Both routers’ interfaces use an OSPF Dead interval of 40.

## Slide 197
Router R15 has been a working part of a network that uses OSPFv2. An engineer then issues the shutdown command in OSPF configuration mode on R15. Which of the following occurs?
R15 empties its IP routing table of all OSPF routes but keeps its LSDB intact.
R15 empties its LSDB but keeps OSPF neighbor relationships active.
R15 keeps OSPF neighbors open but does not accept new OSPF neighbors.
R15 keeps all OSPF configuration but ceases all OSPF activities (routes, LSDB, neighbors)

## Slide 198
Router R15 has been a working part of a network that uses OSPFv2. An engineer then issues the shutdown command in OSPF configuration mode on R15. Which of the following occurs?
R15 empties its IP routing table of all OSPF routes but keeps its LSDB intact.
R15 empties its LSDB but keeps OSPF neighbor relationships active.
R15 keeps OSPF neighbors open but does not accept new OSPF neighbors.
R15 keeps all OSPF configuration but ceases all OSPF activities (routes, LSDB, neighbors)

## Slide 199
Which of the following was a short-term solution to the IPv4 address exhaustion problem?
IP version 6
IP version 5
NAT/PAT
ARP

## Slide 200
Which of the following was a short-term solution to the IPv4 address exhaustion problem?
IP version 6
IP version 5
NAT/PAT
ARP

## Slide 201
A router receives an Ethernet frame that holds an IPv6 packet. The router then makes a decision to route the packet out a serial link. Which of the following statements is true about how a router forwards an IPv6 packet?
The router discards the Ethernet data-link header and trailer of the received frame.
The router makes the forwarding decision based on the packet’s source IPv6 address.
The router keeps the Ethernet header, encapsulating the entire frame inside a new IPv6 packet before sending it over the serial link.
The router uses the IPv4 routing table when choosing where to forward the packet.

## Slide 202
A router receives an Ethernet frame that holds an IPv6 packet. The router then makes a decision to route the packet out a serial link. Which of the following statements is true about how a router forwards an IPv6 packet?
The router discards the Ethernet data-link header and trailer of the received frame.
The router makes the forwarding decision based on the packet’s source IPv6 address.
The router keeps the Ethernet header, encapsulating the entire frame inside a new IPv6 packet before sending it over the serial link.
The router uses the IPv4 routing table when choosing where to forward the packet.

## Slide 203
Which of the following is the shortest valid abbreviation for FE80:0000:0000:0100: 0000:0000:0000:0123?
FE80::100::123
FE8::1::123
FE80::100:0:0:0:123:4567
FE80:0:0:100::123

## Slide 204
Which of the following is the shortest valid abbreviation for FE80:0000:0000:0100: 0000:0000:0000:0123?
FE80::100::123
FE8::1::123
FE80::100:0:0:0:123:4567
FE80:0:0:100::123

## Slide 205
Which of the following is the shortest valid abbreviation for 2000:0300:0040:0005: 6000:0700:0080:0009?
2:3:4:5:6:7:8:9
2000:300:40:5:6000:700:80:9
2000:300:4:5:6000:700:8:9
2000:3:4:5:6:7:8:9

## Slide 206
Which of the following is the shortest valid abbreviation for 2000:0300:0040:0005: 6000:0700:0080:0009?
2:3:4:5:6:7:8:9
2000:300:40:5:6000:700:80:9
2000:300:4:5:6000:700:8:9
2000:3:4:5:6:7:8:9

## Slide 207
Which of the following is the unabbreviated version of IPv6 address 2001:DB8::200:28?
2001:0DB8:0000:0000:0000:0000:0200:0028
2001:0DB8::0200:0028
2001:0DB8:0:0:0:0:0200:0028
2001:0DB8:0000:0000:0000:0000:200:0028

## Slide 208
Which of the following is the unabbreviated version of IPv6 address 2001:DB8::200:28?
2001:0DB8:0000:0000:0000:0000:0200:0028
2001:0DB8::0200:0028
2001:0DB8:0:0:0:0:0200:0028
2001:0DB8:0000:0000:0000:0000:200:0028

## Slide 209
Which of the following is the prefix for address 2000:0000:0000:0005:6000:0700: 0080:0009, assuming a mask of /64?
2000::5::/64
2000::5:0:0:0:0/64
2000:0:0:5::/64
2000:0:0:5:0:0:0:0/64

## Slide 210
Which of the following is the prefix for address 2000:0000:0000:0005:6000:0700: 0080:0009, assuming a mask of /64?
2000::5::/64
2000::5:0:0:0:0/64
2000:0:0:5::/64
2000:0:0:5:0:0:0:0/64

## Slide 211
Which of the following IPv6 addresses appears to be a unique local unicast address, based on its first few hex digits?
3123:1:3:5::1
FE80::1234:56FF:FE78:9ABC
FDAD::1
FF00::5

## Slide 212
Which of the following IPv6 addresses appears to be a unique local unicast address, based on its first few hex digits?
3123:1:3:5::1
FE80::1234:56FF:FE78:9ABC
FDAD::1
FF00::5

## Slide 213
2. Which of the following IPv6 addresses appears to be a global unicast address, based on its first few hex digits?
3123:1:3:5::1
FE80::1234:56FF:FE78:9ABC
FDAD::1
FF00::5

## Slide 214
2. Which of the following IPv6 addresses appears to be a global unicast address, based on its first few hex digits?
3123:1:3:5::1
FE80::1234:56FF:FE78:9ABC
FDAD::1
FF00::5

## Slide 215
When subnetting an IPv6 address block, an engineer shows a drawing that breaks the address structure into three pieces. Comparing this concept to a three-part IPv4 address structure, which part of the IPv6 address structure is most like the IPv4 network part of the address?
Subnet
Interface ID
Network
Global routing prefix
Subnet router anycast

## Slide 216
When subnetting an IPv6 address block, an engineer shows a drawing that breaks the address structure into three pieces. Comparing this concept to a three-part IPv4 address structure, which part of the IPv6 address structure is most like the IPv4 network part of the address?
Subnet
Interface ID
Network
Global routing prefix
Subnet router anycast

## Slide 217
When subnetting an IPv6 address block, an engineer shows a drawing that breaks the address structure into three pieces. Assuming that all subnets use the same prefix length, which of the following answers lists the name of the field on the far right side of the address?
Subnet
Interface ID
Network
Global routing prefix
Subnet router anycast

## Slide 218
When subnetting an IPv6 address block, an engineer shows a drawing that breaks the address structure into three pieces. Assuming that all subnets use the same prefix length, which of the following answers lists the name of the field on the far right side of the address?
Subnet
Interface ID
Network
Global routing prefix
Subnet router anycast

## Slide 219
For the IPv6 address FD00:1234:5678:9ABC:DEF1:2345:6789:ABCD, which part of the address is considered the global ID of the unique local address?
None; this address has no global ID.
00:1234:5678:9ABC
DEF1:2345:6789:ABCD
00:1234:5678
FD00

## Slide 220
For the IPv6 address FD00:1234:5678:9ABC:DEF1:2345:6789:ABCD, which part of the address is considered the global ID of the unique local address?
None; this address has no global ID.
00:1234:5678:9ABC
DEF1:2345:6789:ABCD
00:1234:5678
FD00

## Slide 221
Router R1 has an interface named Gigabit Ethernet 0/1, whose MAC address has been set to 0200.0001.000A. Which of the following commands, added in R1’s Gigabit Ethernet 0/1 configuration mode, gives this router’s G0/1 interface a unicast IPv6 address of 2001:1:1:1:1:200:1:A, with a /64 prefix length?
ipv6 address 2001:1:1:1:1:200:1:A/64
ipv6 address 2001:1:1:1:1:200:1:A/64 eui-64
ipv6 address 2001:1:1:1:1:200:1:A /64 eui-64
ipv6 address 2001:1:1:1:1:200:1:A /64
None of the other answers are correct.

## Slide 222
Router R1 has an interface named Gigabit Ethernet 0/1, whose MAC address has been set to 0200.0001.000A. Which of the following commands, added in R1’s Gigabit Ethernet 0/1 configuration mode, gives this router’s G0/1 interface a unicast IPv6 address of 2001:1:1:1:1:200:1:A, with a /64 prefix length?
ipv6 address 2001:1:1:1:1:200:1:A/64
ipv6 address 2001:1:1:1:1:200:1:A/64 eui-64
ipv6 address 2001:1:1:1:1:200:1:A /64 eui-64
ipv6 address 2001:1:1:1:1:200:1:A /64
None of the other answers are correct.

## Slide 223
Router R1 has an interface named Gigabit Ethernet 0/1, whose MAC address has been set to 5055.4444.3333. This interface has been configured with the ipv6 address 2000:1:1:1::/64 eui-64 subcommand. What unicast address will this interface use?
2000:1:1:1:52FF:FE55:4444:3333
2000:1:1:1:5255:44FF:FE44:3333
2000:1:1:1:5255:4444:33FF:FE33
2000:1:1:1:200:FF:FE00:0 .

## Slide 224
Router R1 has an interface named Gigabit Ethernet 0/1, whose MAC address has been set to 5055.4444.3333. This interface has been configured with the ipv6 address 2000:1:1:1::/64 eui-64 subcommand. What unicast address will this interface use?
2000:1:1:1:52FF:FE55:4444:3333
2000:1:1:1:5255:44FF:FE44:3333
2000:1:1:1:5255:4444:33FF:FE33
2000:1:1:1:200:FF:FE00:0 .

## Slide 225
Router R1 currently supports IPv4, routing packets in and out all its interfaces. R1’s configuration needs to be migrated to support dual-stack operation, routing both IPv4 and IPv6. Which of the following tasks must be performed before the router can also support routing IPv6 packets? (Choose two answers.)
Enable IPv6 on each interface using an ipv6 address interface subcommand.
Enable support for both versions with the ip versions 4 6 global command.
Additionally enable IPv6 routing using the ipv6 unicast-routing global command.
Migrate to dual-stack routing using the ip routing dual-stack global command.

## Slide 226
Router R1 currently supports IPv4, routing packets in and out all its interfaces. R1’s configuration needs to be migrated to support dual-stack operation, routing both IPv4 and IPv6. Which of the following tasks must be performed before the router can also support routing IPv6 packets? (Choose two answers.)
Enable IPv6 on each interface using an ipv6 address interface subcommand.
Enable support for both versions with the ip versions 4 6 global command.
Additionally enable IPv6 routing using the ipv6 unicast-routing global command.
Migrate to dual-stack routing using the ip routing dual-stack global command.

## Slide 227
Router R1 has an interface named Gigabit Ethernet 0/1, whose MAC address has been set to 0200.0001.000A. The interface is then configured with the ipv6 address 2001:1:1:1:200:FF:FE01:B/64 interface subcommand; no other ipv6 address commands are configured on the interface. Which of the following answers lists the linklocal address used on the interface?
FE80::FF:FE01:A
FE80::FF:FE01:B
FE80::200:FF:FE01:A
FE80::200:FF:FE01:B

## Slide 228
Router R1 has an interface named Gigabit Ethernet 0/1, whose MAC address has been set to 0200.0001.000A. The interface is then configured with the ipv6 address 2001:1:1:1:200:FF:FE01:B/64 interface subcommand; no other ipv6 address commands are configured on the interface. Which of the following answers lists the linklocal address used on the interface?
FE80::FF:FE01:A
FE80::FF:FE01:B
FE80::200:FF:FE01:A
FE80::200:FF:FE01:B

## Slide 229
Which of the following multicast addresses is defined as the address for sending packets to only the IPv6 routers on the local link?
FF02::1
FF02::2
FF02::5
FF02::A

## Slide 230
Which of the following multicast addresses is defined as the address for sending packets to only the IPv6 routers on the local link?
FF02::1
FF02::2
FF02::5
FF02::A

## Slide 231
A router has been configured with the ipv6 address 2000:1:2:3::1/64 command on its G0/1 interface as shown in the figure. The router creates a link-local address of FE80::FF:FE00:1 as well. The interface is working. Which of the following routes will the router add to its IPv6 routing table? (Choose two answers.)
A route for 2000:1:2:3::/64
A route for FE80::FF:FE00:1/64
A route for 2000:1:2:3::1/128
A route for FE80::FF:FE00:1/128

## Slide 232
A router has been configured with the ipv6 address 2000:1:2:3::1/64 command on its G0/1 interface as shown in the figure. The router creates a link-local address of FE80::FF:FE00:1 as well. The interface is working. Which of the following routes will the router add to its IPv6 routing table? (Choose two answers.)
A route for 2000:1:2:3::/64
A route for FE80::FF:FE00:1/64
A route for 2000:1:2:3::1/128
A route for FE80::FF:FE00:1/128

## Slide 233
A router has been configured with the ipv6 address 3111:1:1:1::1/64 command on its G0/1 interface and ipv6 address 3222:2:2:2::1/64 on its G0/2 interface. Both interfaces are working. Which of the following routes would you expect to see in the output of the show ipv6 route connected command? (Choose two answers.)
A route for 3111:1:1:1::/64
A route for 3111:1:1:1::1/64
A route for 3222:2:2:2::/64
A route for 3222:2:2:2::2/128

## Slide 234
A router has been configured with the ipv6 address 3111:1:1:1::1/64 command on its G0/1 interface and ipv6 address 3222:2:2:2::1/64 on its G0/2 interface. Both interfaces are working. Which of the following routes would you expect to see in the output of the show ipv6 route connected command? (Choose two answers.)
A route for 3111:1:1:1::/64
A route for 3111:1:1:1::1/64
A route for 3222:2:2:2::/64
A route for 3222:2:2:2::2/128

## Slide 235
PC1, PC2, and Router R1 all connect to the same VLAN and IPv6 subnet. PC1 wants to send its first IPv6 packet to PC2. What protocol or message will PC1 use to discover the MAC address to which PC1 should send the Ethernet frame that encapsulates this IPv6 packet?
ARP
DNS
NDP
SLAAC

## Slide 236
PC1, PC2, and Router R1 all connect to the same VLAN and IPv6 subnet. PC1 wants to send its first IPv6 packet to PC2. What protocol or message will PC1 use to discover the MAC address to which PC1 should send the Ethernet frame that encapsulates this IPv6 packet?
ARP
DNS
NDP
SLAAC

## Slide 237
Which of the following pieces of information does a router supply in an NDP Router Advertisement (RA) message? (Choose two answers.)
Router IPv6 address
Host name of the router
IPv6 prefix(es) on the link
IPv6 address of DHCP server

## Slide 238
Which of the following pieces of information does a router supply in an NDP Router Advertisement (RA) message? (Choose two answers.)
Router IPv6 address
Host name of the router
IPv6 prefix(es) on the link
IPv6 address of DHCP server

## Slide 239
Wired Ethernet and Wi-Fi are based on which two IEEE standards, respectively?
802.1, 802.3
802.3, 802.1
802.3, 802.11
802.11, 802.3

## Slide 240
Wired Ethernet and Wi-Fi are based on which two IEEE standards, respectively?
802.1, 802.3
802.3, 802.1
802.3, 802.11
802.11, 802.3

## Slide 241
. Devices using a wireless LAN must operate in which one of the following modes?
Round-robin access
Half duplex
Full duplex
None of these answers

## Slide 242
. Devices using a wireless LAN must operate in which one of the following modes?
Round-robin access
Half duplex
Full duplex
None of these answers

## Slide 243
An access point is set up to offer wireless coverage in an office. Which one of the following is the correct 802.11 term for the resulting standalone network?
BSA
BSD
BSS
IBSS

## Slide 244
An access point is set up to offer wireless coverage in an office. Which one of the following is the correct 802.11 term for the resulting standalone network?
BSA
BSD
BSS
IBSS

## Slide 245
Which one of the following is used to uniquely identify an AP and the basic service set it maintains with its associated wireless clients?
SSID
BSSID
Ethernet MAC address
Radio MAC address

## Slide 246
Which one of the following is used to uniquely identify an AP and the basic service set it maintains with its associated wireless clients?
SSID
BSSID
Ethernet MAC address
Radio MAC address

## Slide 247
Which one of the following can be used to provide wireless connectivity to a nonwireless device?
Wireless repeater
Workgroup bridge
Transparent bridge
Adaptive bridge

## Slide 248
Which one of the following can be used to provide wireless connectivity to a nonwireless device?
Wireless repeater
Workgroup bridge
Transparent bridge
Adaptive bridge

## Slide 249
Which one of the following is not needed in a Cisco outdoor mesh network?
A BSS function
Ethernet cabling to each AP
A workgroup bridge
A backhaul network

## Slide 250
Which one of the following is not needed in a Cisco outdoor mesh network?
A BSS function
Ethernet cabling to each AP
A workgroup bridge
A backhaul network

## Slide 251
Which of the following are frequency bands commonly used for Wi-Fi?
2.5 KHz
2.5 MHz
5 MHz
2.5 GHz
5 GHz

## Slide 252
Which of the following are frequency bands commonly used for Wi-Fi?
2.5 KHz
2.5 MHz
5 MHz
2.5 GHz
5 GHz

## Slide 253
Which of the following are considered to be nonoverlapping channels?
Channels 1, 2, and 3 in the 2.4-GHz band
Channels 1, 5, and 10 in the 2.4-GHz band
Channels 1, 6, and 11 in the 2.4-GHz band
Channels 40, 44, and 48 in the 5-GHz band

## Slide 254
Which of the following are considered to be nonoverlapping channels?
Channels 1, 2, and 3 in the 2.4-GHz band
Channels 1, 5, and 10 in the 2.4-GHz band
Channels 1, 6, and 11 in the 2.4-GHz band
Channels 40, 44, and 48 in the 5-GHz band

## Slide 255
Which one of the following terms best describes a Cisco wireless access point that operates in a standalone, independent manner?
Autonomous AP
Independent AP
Lightweight AP
Embedded AP

## Slide 256
Which one of the following terms best describes a Cisco wireless access point that operates in a standalone, independent manner?
Autonomous AP
Independent AP
Lightweight AP
Embedded AP

## Slide 257
The Cisco Meraki cloud-based APs are most accurately described by which one of the following statements?
Autonomous APs joined to a WLC
Autonomous APs centrally managed
Lightweight APs joined to a WLC
Lightweight APs centrally managed

## Slide 258
The Cisco Meraki cloud-based APs are most accurately described by which one of the following statements?
Autonomous APs joined to a WLC
Autonomous APs centrally managed
Lightweight APs joined to a WLC
Lightweight APs centrally managed

## Slide 259
A lightweight access point is said to participate in which one of the following architectures?
Light-MAC
Tunnel-MAC
Split-MAC
Big-MAC

## Slide 260
A lightweight access point is said to participate in which one of the following architectures?
Light-MAC
Tunnel-MAC
Split-MAC
Big-MAC

## Slide 261
How does a lightweight access point communicate with a wireless LAN controller?
Through an IPsec tunnel
Through a CAPWAP tunnel
Through a GRE tunnel
Directly over Layer 2

## Slide 262
How does a lightweight access point communicate with a wireless LAN controller?
Through an IPsec tunnel
Through a CAPWAP tunnel
Through a GRE tunnel
Directly over Layer 2

## Slide 263
Which one of the following is not needed for a lightweight AP in default local mode to be able to support three SSIDs that are bound to three VLANs?
A trunk link carrying three VLANs
An access link bound to a single VLAN
A WLC connected to three VLANs
A CAPWAP tunnel to a WLC

## Slide 264
Which one of the following is not needed for a lightweight AP in default local mode to be able to support three SSIDs that are bound to three VLANs?
A trunk link carrying three VLANs
An access link bound to a single VLAN
A WLC connected to three VLANs
A CAPWAP tunnel to a WLC

## Slide 265
Which one of the following WLC deployment models would be best for a large enterprise with around 3000 lightweight APs?
Cisco Mobility Express
Embedded
Unified
Cloud-based

## Slide 266
Which one of the following WLC deployment models would be best for a large enterprise with around 3000 lightweight APs?
Cisco Mobility Express
Embedded
Unified
Cloud-based

## Slide 267
If a lightweight AP provides at least one BSS for wireless clients, which one of the following modes does it use?
Local
Normal
Monitor
Client

## Slide 268
Regarding lightweight AP modes, which one of the following is true?
An AP can operate in multiple modes at the same time.
An AP only has one possible mode of operation.
The Run mode is the default mode.
The SE-Connect mode is used for spectrum analysis

## Slide 269
Which of the following are necessary components of a secure wireless connection? (Choose all that apply.)
Encryption
MIC
Authentication
All of these answers are correct.

## Slide 270
Which of the following are necessary components of a secure wireless connection? (Choose all that apply.)
Encryption
MIC
Authentication
All of these answers are correct.

## Slide 271
Which one of the following is used to protect the integrity of data in a wireless frame?
WIPS
WEP
MIC
EAP

## Slide 272
Which one of the following is used to protect the integrity of data in a wireless frame?
WIPS
WEP
MIC
EAP

## Slide 273
Which one of the following is a wireless encryption method that has been found to be vulnerable and is not recommended for use?
AES
WPA
EAP
WEP

## Slide 274
Which one of the following is a wireless encryption method that has been found to be vulnerable and is not recommended for use?
AES
WPA
EAP
WEP

## Slide 275
Which one of the following is used as the authentication framework when 802.1x is used on a WLAN?
Open authentication
WEP
EAP
WPA

## Slide 276
Which one of the following is used as the authentication framework when 802.1x is used on a WLAN?
Open authentication
WEP
EAP
WPA

## Slide 277
Suppose you would like to select a method to protect the privacy and integrity of wireless data. Which one of the following methods should you avoid because it has been deprecated ?
TKIP
CCMP
GCMP
EAP

## Slide 278
Suppose you would like to select a method to protect the privacy and integrity of wireless data. Which one of the following methods should you avoid because it has been deprecated ?
TKIP
CCMP
GCMP
EAP

## Slide 279
Which one of the following is the data encryption and integrity method used by WPA2?
WEP
TKIP
CCMP
WPA

## Slide 280
Which one of the following is the data encryption and integrity method used by WPA2?
WEP
TKIP
CCMP
WPA

## Slide 281
The Wi-Fi Alliance offers which of the following certifications for wireless devices that correctly implement security standards?
WEP
WPA2
802.11
AES

## Slide 282
The Wi-Fi Alliance offers which of the following certifications for wireless devices that correctly implement security standards?
WEP
WPA2
802.11
AES

## Slide 283
A pre-shared key is used in which of the following wireless security configurations? (Choose all that apply.)
WPA2 personal mode
WPA2 enterprise mode
WPA3 personal mode
WPA3 enterprise mode

## Slide 284
A pre-shared key is used in which of the following wireless security configurations? (Choose all that apply.)
WPA2 personal mode
WPA2 enterprise mode
WPA3 personal mode
WPA3 enterprise mode

## Slide 285
Suppose you need to connect a lightweight AP to a network. Which one of the following link types would be necessary?
Access mode link
Trunk mode link
LAG mode link
EtherChannel link

## Slide 286
Suppose you need to connect a lightweight AP to a network. Which one of the following link types would be necessary?
Access mode link
Trunk mode link
LAG mode link
EtherChannel link

## Slide 287
An autonomous AP will be configured to support three WLANs that correspond to three VLANs. The AP will connect to the network over which one of the following?
Access mode link
Trunk mode link
LAG mode link
EtherChannel link

## Slide 288
An autonomous AP will be configured to support three WLANs that correspond to three VLANs. The AP will connect to the network over which one of the following?
Access mode link
Trunk mode link
LAG mode link
EtherChannel link

## Slide 289
Suppose you would like to connect to a WLC to configure a new WLAN on it. Which one of the following is a valid method to use?
SSH
HTTPS
HTTP
All of these answers are correct.

## Slide 290
Suppose you would like to connect to a WLC to configure a new WLAN on it. Which one of the following is a valid method to use?
SSH
HTTPS
HTTP
All of these answers are correct.

## Slide 291
Which one of the following correctly describes the single logical link formed by bundling all of a controller’s distribution system ports together?
PHY
DSP
LAG
GEC

## Slide 292
Which one of the following correctly describes the single logical link formed by bundling all of a controller’s distribution system ports together?
PHY
DSP
LAG
GEC

## Slide 293
Which one of the following controller interfaces maps a WLAN to a VLAN?
Bridge interface
Virtual interface
WLAN interface
Dynamic interface

## Slide 294
Which one of the following controller interfaces maps a WLAN to a VLAN?
Bridge interface
Virtual interface
WLAN interface
Dynamic interface

## Slide 295
Which two of the following things are bound together when a new WLAN is created?
VLAN
AP
Controller interface
SSID

## Slide 296
Which two of the following things are bound together when a new WLAN is created?
VLAN
AP
Controller interface
SSID

## Slide 297
What is the maximum number of WLANs you can configure on a Cisco wireless controller?
8
16
512
1024

## Slide 298
What is the maximum number of WLANs you can configure on a Cisco wireless controller?
8
16
512
1024

## Slide 299
Which of the following parameters are necessary when creating a new WLAN with the controller GUI? (Choose all that apply.)
SSID
VLAN number
Interface
BSSID
IP subnet

## Slide 300
Which of the following parameters are necessary when creating a new WLAN with the controller GUI? (Choose all that apply.)
SSID
VLAN number
Interface
BSSID
IP subnet

## Slide 301
Which of the following header fields identify which TCP/IP application gets data received by the computer? (Choose two answers.)
Ethernet Type
SNAP Protocol Type
IP Protocol
TCP Port Number
UDP Port Number

## Slide 302
Which of the following header fields identify which TCP/IP application gets data received by the computer? (Choose two answers.)
Ethernet Type
SNAP Protocol Type
IP Protocol
TCP Port Number
UDP Port Number

## Slide 303
2. Which of the following are typical functions of TCP? (Choose four answers.)
Flow control (windowing)
Error recovery
Multiplexing using port numbers
Routing
Encryption
Ordered data transfer

## Slide 304
2. Which of the following are typical functions of TCP? (Choose four answers.)
Flow control (windowing)
Error recovery
Multiplexing using port numbers
Routing
Encryption
Ordered data transfer

## Slide 305
3. Which of the following functions is performed by both TCP and UDP?
Windowing
Error recovery
Multiplexing using port numbers
Routing
Encryption
Ordered data transfer

## Slide 306
3. Which of the following functions is performed by both TCP and UDP?
Windowing
Error recovery
Multiplexing using port numbers
Routing
Encryption
Ordered data transfer

## Slide 307
4. What do you call data that includes the Layer 4 protocol header, and data given to Layer 4 by the upper layers, not including any headers and trailers from Layers 1 to 3? (Choose two answers.)
L3PDU
Chunk
Segment
Packet
Frame
L4PDU

## Slide 308
4. What do you call data that includes the Layer 4 protocol header, and data given to Layer 4 by the upper layers, not including any headers and trailers from Layers 1 to 3? (Choose two answers.)
L3PDU
Chunk
Segment
Packet
Frame
L4PDU

## Slide 309
5. In the URI http://blog.certskills.com/config-labs, which part identifies the web server?
http
blog.certskills.com
certskills.com
http://blog.certskills.com
The file name.html includes the hostname.

## Slide 310
5. In the URI http://blog.certskills.com/config-labs, which part identifies the web server?
http
blog.certskills.com
certskills.com
http://blog.certskills.com
The file name.html includes the hostname.

## Slide 311
6. Fred opens a web browser and connects to the www.certskills.com website. Which of the following are typically true about what happens between Fred’s web browser and the web server? (Choose two answers.)
Messages flowing toward the server use UDP destination port 80.
Messages flowing from the server typically use RTP.
Messages flowing to the client typically use a source TCP port number of 80.
Messages flowing to the server typically use TCP

## Slide 312
6. Fred opens a web browser and connects to the www.certskills.com website. Which of the following are typically true about what happens between Fred’s web browser and the web server? (Choose two answers.)
Messages flowing toward the server use UDP destination port 80.
Messages flowing from the server typically use RTP.
Messages flowing to the client typically use a source TCP port number of 80.
Messages flowing to the server typically use TCP

## Slide 313
Barney is a host with IP address 10.1.1.1 in subnet 10.1.1.0/24. Which of the following are things that a standard IP ACL could be configured to do? (Choose two answers.)
Match the exact source IP address.
Match IP addresses 10.1.1.1 through 10.1.1.4 with one access-list command without matching other IP addresses.
Match all IP addresses in Barney’s subnet with one access-list command without matching other IP addresses.
Match only the packet’s destination IP address.

## Slide 314
Barney is a host with IP address 10.1.1.1 in subnet 10.1.1.0/24. Which of the following are things that a standard IP ACL could be configured to do? (Choose two answers.)
Match the exact source IP address.
Match IP addresses 10.1.1.1 through 10.1.1.4 with one access-list command without matching other IP addresses.
Match all IP addresses in Barney’s subnet with one access-list command without matching other IP addresses.
Match only the packet’s destination IP address.

## Slide 315
2. Which of the following answers list a valid number that can be used with standard numbered IP ACLs? (Choose two answers.)
1987
2187
187
87

## Slide 316
2. Which of the following answers list a valid number that can be used with standard numbered IP ACLs? (Choose two answers.)
1987
2187
187
87

## Slide 317
3. Which of the following wildcard masks is most useful for matching all IP packets in subnet 10.1.128.0, mask 255.255.255.0?
0.0.0.0
0.0.0.31
0.0.0.240
0.0.0.255
0.0.15.0
0.0.248.255

## Slide 318
3. Which of the following wildcard masks is most useful for matching all IP packets in subnet 10.1.128.0, mask 255.255.255.0?
0.0.0.0
0.0.0.31
0.0.0.240
0.0.0.255
0.0.15.0
0.0.248.255

## Slide 319
4. Which of the following wildcard masks is most useful for matching all IP packets in subnet 10.1.128.0, mask 255.255.240.0?
0.0.0.0
0.0.0.31
0.0.0.240
0.0.0.255
0.0.15.255
0.0.248.255

## Slide 320
4. Which of the following wildcard masks is most useful for matching all IP packets in subnet 10.1.128.0, mask 255.255.240.0?
0.0.0.0
0.0.0.31
0.0.0.240
0.0.0.255
0.0.15.255
0.0.248.255

## Slide 321
5. ACL 1 has three statements, in the following order, with address and wildcard mask values as follows: 1.0.0.0 0.255.255.255, 1.1.0.0 0.0.255.255, and 1.1.1.0 0.0.0.255. If a router tried to match a packet sourced from IP address 1.1.1.1 using this ACL, which ACL statement does a router consider the packet to have matched?
First
Second
Third
Implied deny at the end of the ACL

## Slide 322
5. ACL 1 has three statements, in the following order, with address and wildcard mask values as follows: 1.0.0.0 0.255.255.255, 1.1.0.0 0.0.255.255, and 1.1.1.0 0.0.0.255. If a router tried to match a packet sourced from IP address 1.1.1.1 using this ACL, which ACL statement does a router consider the packet to have matched?
First
Second
Third
Implied deny at the end of the ACL

## Slide 323
6. Which of the following access-list commands matches all packets sent from hosts in subnet 172.16.4.0/23?
access-list 1 permit 172.16.0.5 0.0.255.0
access-list 1 permit 172.16.4.0 0.0.1.255
access-list 1 permit 172.16.5.0
access-list 1 permit 172.16.5.0 0.0.0.127

## Slide 324
6. Which of the following access-list commands matches all packets sent from hosts in subnet 172.16.4.0/23?
access-list 1 permit 172.16.0.5 0.0.255.0
access-list 1 permit 172.16.4.0 0.0.1.255
access-list 1 permit 172.16.5.0
access-list 1 permit 172.16.5.0 0.0.0.127

## Slide 325
Which of the following fields cannot be compared based on an extended IP ACL? (Choose two answers.)
Protocol
Source IP address
Destination IP address
TOS byte e. URL
Filename for FTP transfers

## Slide 326
Which of the following fields cannot be compared based on an extended IP ACL? (Choose two answers.)
Protocol
Source IP address
Destination IP address
TOS byte
URL
Filename for FTP transfers

## Slide 327
2. Which of the following access-list commands permit packets going from host 10.1.1.1 to all web servers whose IP addresses begin with 172.16.5? (Choose two answers.)
access-list 101 permit tcp host 10.1.1.1 172.16.5.0 0.0.0.255 eq www
access-list 1951 permit ip host 10.1.1.1 172.16.5.0 0.0.0.255 eq www
access-list 2523 permit ip host 10.1.1.1 eq www 172.16.5.0 0.0.0.255
access-list 2523 permit tcp host 10.1.1.1 eq www 172.16.5.0 0.0.0.255
access-list 2523 permit tcp host 10.1.1.1 172.16.5.0 0.0.0.255 eq www

## Slide 328
2. Which of the following access-list commands permit packets going from host 10.1.1.1 to all web servers whose IP addresses begin with 172.16.5? (Choose two answers.)
access-list 101 permit tcp host 10.1.1.1 172.16.5.0 0.0.0.255 eq www
access-list 1951 permit ip host 10.1.1.1 172.16.5.0 0.0.0.255 eq www
access-list 2523 permit ip host 10.1.1.1 eq www 172.16.5.0 0.0.0.255
access-list 2523 permit tcp host 10.1.1.1 eq www 172.16.5.0 0.0.0.255
access-list 2523 permit tcp host 10.1.1.1 172.16.5.0 0.0.0.255 eq www

## Slide 329
3. Which of the following access-list commands permits packets going to any web client from all web servers whose IP addresses begin with 172.16.5?
access-list 101 permit tcp host 10.1.1.1 172.16.5.0 0.0.0.255 eq www
access-list 1951 permit ip host 10.1.1.1 172.16.5.0 0.0.0.255 eq www
access-list 2523 permit tcp any eq www 172.16.5.0 0.0.0.255
access-list 2523 permit tcp 172.16.5.0 0.0.0.255 eq www 172.16.5.0 0.0.0.255
access-list 2523 permit tcp 172.16.5.0 0.0.0.255 eq www any

## Slide 330
3. Which of the following access-list commands permits packets going to any web client from all web servers whose IP addresses begin with 172.16.5?
access-list 101 permit tcp host 10.1.1.1 172.16.5.0 0.0.0.255 eq www
access-list 1951 permit ip host 10.1.1.1 172.16.5.0 0.0.0.255 eq www
access-list 2523 permit tcp any eq www 172.16.5.0 0.0.0.255
access-list 2523 permit tcp 172.16.5.0 0.0.0.255 eq www 172.16.5.0 0.0.0.255
access-list 2523 permit tcp 172.16.5.0 0.0.0.255 eq www any

## Slide 331
4. In a router running a recent IOS version (at least version 15.0), an engineer needs to delete the second line in ACL 101, which currently has four commands configured. Which of the following options could be used? (Choose two answers.)
Delete the entire ACL and reconfigure the three ACL statements that should remain in the ACL.
Delete one line from the ACL using the no access-list… global command.
Delete one line from the ACL by entering ACL configuration mode for the ACL and then deleting only the second line based on its sequence number.
Delete the last three lines from the ACL from global configuration mode, and then add the last two statements back into the ACL.

## Slide 332
4. In a router running a recent IOS version (at least version 15.0), an engineer needs to delete the second line in ACL 101, which currently has four commands configured. Which of the following options could be used? (Choose two answers.)
Delete the entire ACL and reconfigure the three ACL statements that should remain in the ACL.
Delete one line from the ACL using the no access-list… global command.
Delete one line from the ACL by entering ACL configuration mode for the ACL and then deleting only the second line based on its sequence number.
Delete the last three lines from the ACL from global configuration mode, and then add the last two statements back into the ACL.

## Slide 333
6. An engineer configures an ACL but forgets to save the configuration. At that point, which of the following commands display the configuration of an IPv4 ACL, including line numbers? (Choose two answers.)
show running-config
show startup-config
show ip access-lists
show access-lists

## Slide 334
6. An engineer configures an ACL but forgets to save the configuration. At that point, which of the following commands display the configuration of an IPv4 ACL, including line numbers? (Choose two answers.)
show running-config
show startup-config
show ip access-lists
show access-lists

## Slide 335
Which one of the following terms means anything that can be considered to be a weakness that can compromise security?
Exploit
Vulnerability
Attack
Threat

## Slide 336
Which one of the following terms means anything that can be considered to be a weakness that can compromise security?
Exploit
Vulnerability
Attack
Threat

## Slide 337
2. An actual potential to exploit a vulnerability is known as which one of the following terms?
Vulnerability
Attack
Exploit
Threat

## Slide 338
2. An actual potential to exploit a vulnerability is known as which one of the following terms?
Vulnerability
Attack
Exploit
Threat

## Slide 339
3. In a spoofing attack, which of the following parameters are commonly spoofed? (Choose two answers.)
MAC address
Source IP address
Destination IP address
ARP address

## Slide 340
3. In a spoofing attack, which of the following parameters are commonly spoofed? (Choose two answers.)
MAC address
Source IP address
Destination IP address
ARP address

## Slide 341
4. Suppose an attacker sends a series of packets toward a destination IP address with the TCP SYN flag set but sends no other packet types. Which of the following attacks is likely taking place?
Spoofing attack
Reflection attack
Reconnaissance attack
Denial-of-service attack
None of the choices are correct.

## Slide 342
4. Suppose an attacker sends a series of packets toward a destination IP address with the TCP SYN flag set but sends no other packet types. Which of the following attacks is likely taking place?
Spoofing attack
Reflection attack
Reconnaissance attack
Denial-of-service attack
None of the choices are correct.

## Slide 343
5. In a reflection attack, the source IP address in the attack packets is spoofed so that it contains which one of the following entities?
The address of the attacker
The address of the reflector
The address of the victim
The address of the router

## Slide 344
5. In a reflection attack, the source IP address in the attack packets is spoofed so that it contains which one of the following entities?
The address of the attacker
The address of the reflector
The address of the victim
The address of the router

## Slide 345
6. During a successful man-in-the-middle attack, which two of the following actions is an attacker most likely to perform?
Eavesdrop on traffic passing between hosts
Induce a buffer overflow on multiple hosts
Modify data passing between hosts
Use ping sweeps and port scans to discover the network

## Slide 346
6. During a successful man-in-the-middle attack, which two of the following actions is an attacker most likely to perform?
Eavesdrop on traffic passing between hosts
Induce a buffer overflow on multiple hosts
Modify data passing between hosts
Use ping sweeps and port scans to discover the network

## Slide 347
7. Which one of the following is the goal of a brute-force attack?
Try every possible TCP port until a service answers
Try every possible combination of keyboard characters to guess a user’s password
Initiate a denial-of-service operation on every possible host in a subnet
Spoof every possible IP address in an organization

## Slide 348
7. Which one of the following is the goal of a brute-force attack?
Try every possible TCP port until a service answers
Try every possible combination of keyboard characters to guess a user’s password
Initiate a denial-of-service operation on every possible host in a subnet
Spoof every possible IP address in an organization

## Slide 349
8. Which one of the following is an example of a AAA server?
DHCP
DNS
SNMP
ISE

## Slide 350
8. Which one of the following is an example of a AAA server?
DHCP
DNS
SNMP
ISE

## Slide 351
9. Physical access control is important for which one of the following reasons?
It prevents unauthorized people from sitting at a corporate user’s desk and using their computer.
It prevents users from getting angry and damaging computer equipment.
It prevents unauthorized access to network closets.
It prevents fires from destroying data centers

## Slide 352
9. Physical access control is important for which one of the following reasons?
It prevents unauthorized people from sitting at a corporate user’s desk and using their computer.
It prevents users from getting angry and damaging computer equipment.
It prevents unauthorized access to network closets.
It prevents fires from destroying data centers

## Slide 353
Imagine that you have configured the enable secret command, followed by the enable password command, from the console. You log out of the switch and log back in at the console. Which command defines the password that you had to enter to access privileged mode?
a. enable password
b. enable secret
c. Neither
d. The password command, if it’s configured

## Slide 354
Imagine that you have configured the enable secret command, followed by the enable password command, from the console. You log out of the switch and log back in at the console. Which command defines the password that you had to enter to access privileged mode?
a. enable password
b. enable secret
c. Neither
d. The password command, if it’s configured

## Slide 355
2. Some IOS commands store passwords as clear text, but you can then encrypt the passwords with the service password-encryption global command. By comparison, other commands store a computed hash of the password instead of storing the password. Comparing the two options, which one answer is the most accurate about why one method is better than the other?
Using hashes is preferred because encrypted IOS passwords can be easily decrypted.
Using hashes is preferred because of the large CPU effort required for encryption.
Using encryption is preferred because it provides stronger password protection.
Using encryption is preferred because of the large CPU effort required for hashes.

## Slide 356
2. Some IOS commands store passwords as clear text, but you can then encrypt the passwords with the service password-encryption global command. By comparison, other commands store a computed hash of the password instead of storing the password. Comparing the two options, which one answer is the most accurate about why one method is better than the other?
Using hashes is preferred because encrypted IOS passwords can be easily decrypted.
Using hashes is preferred because of the large CPU effort required for encryption.
Using encryption is preferred because it provides stronger password protection.
Using encryption is preferred because of the large CPU effort required for hashes.

## Slide 357
3. A network engineer issues a show running-config command and sees only one line of output that mentions the enable secret command, as follows: enable secret 5 $1$ZGMA$e8cmvkz4UjiJhVp7.maLE1 Which of the following is true about users of this router?
A user must type $1$ZGMA$e8cmvkz4UjiJhVp7.maLE1 to reach enable mode.
The router will hash the clear-text password that the user types to compare to the hashed password.
A no service password-encryption configuration command would decrypt this password.
The router will decrypt the password in the configuration to compare to the clear-text password typed by the user.

## Slide 358
3. A network engineer issues a show running-config command and sees only one line of output that mentions the enable secret command, as follows: enable secret 5 $1$ZGMA$e8cmvkz4UjiJhVp7.maLE1 Which of the following is true about users of this router?
A user must type $1$ZGMA$e8cmvkz4UjiJhVp7.maLE1 to reach enable mode.
The router will hash the clear-text password that the user types to compare to the hashed password.
A no service password-encryption configuration command would decrypt this password.
The router will decrypt the password in the configuration to compare to the clear-text password typed by the user.

## Slide 359
4. A single-line ACL has been added to a router configuration using the command ip access-list 1 permit 172.16.4.0 0.0.1.255. The configuration also includes the access-class 1 in command in VTY configuration mode. Which answer accurately describes how the router uses ACL 1?
Hosts in subnet 172.16.4.0/23 alone can telnet into the router.
CLI users cannot telnet from the router to hosts in subnet 172.16.4.0/23 alone.
Hosts in subnet 172.16.4.0/23 alone can log in but cannot reach enable mode of the router.
The router will only forward packets with source addresses in subnet 172.16.4.0/23.

## Slide 360
4. A single-line ACL has been added to a router configuration using the command ip access-list 1 permit 172.16.4.0 0.0.1.255. The configuration also includes the access-class 1 in command in VTY configuration mode. Which answer accurately describes how the router uses ACL 1?
Hosts in subnet 172.16.4.0/23 alone can telnet into the router.
CLI users cannot telnet from the router to hosts in subnet 172.16.4.0/23 alone.
Hosts in subnet 172.16.4.0/23 alone can log in but cannot reach enable mode of the router.
The router will only forward packets with source addresses in subnet 172.16.4.0/23.

## Slide 361
5. A next-generation firewall sits at the edge of a company’s connection to the Internet. It has been configured to prevent Telnet clients residing in the Internet from accessing Telnet servers inside the company. Which of the following might a next-generation firewall use that a traditional firewall would not?
Match message destination well-known port 23
Match message application data
Match message IP protocol 23
Match message source TCP ports greater than 49152

## Slide 362
5. A next-generation firewall sits at the edge of a company’s connection to the Internet. It has been configured to prevent Telnet clients residing in the Internet from accessing Telnet servers inside the company. Which of the following might a next-generation firewall use that a traditional firewall would not?
Match message destination well-known port 23
Match message application data
Match message IP protocol 23
Match message source TCP ports greater than 49152

## Slide 363
6. Which actions show a behavior typically supported by a Cisco next-generation IPS (NGIPS) beyond the capabilities of a traditional IPS? (Choose two answers)
Gather and use host-based information for context
Comparisons between messages and a database of exploit signatures
Logging events for later review by the security team
Filter URIs using reputation scores

## Slide 364
6. Which actions show a behavior typically supported by a Cisco next-generation IPS (NGIPS) beyond the capabilities of a traditional IPS? (Choose two answers)
Gather and use host-based information for context
Comparisons between messages and a database of exploit signatures
Logging events for later review by the security team
Filter URIs using reputation scores

## Slide 365
Which of the following is required when configuring port security with sticky learning?
Setting the maximum number of allowed MAC addresses on the interface with the switchport port-security maximum interface subcommand.
Enabling port security with the switchport port-security interface subcommand.
Defining the specific allowed MAC addresses using the switchport port-security mac-address interface subcommand.
All the other answers list required commands.

## Slide 366
Which of the following is required when configuring port security with sticky learning?
Setting the maximum number of allowed MAC addresses on the interface with the switchport port-security maximum interface subcommand.
Enabling port security with the switchport port-security interface subcommand.
Defining the specific allowed MAC addresses using the switchport port-security mac-address interface subcommand.
All the other answers list required commands.

## Slide 367
2. A Cisco Catalyst switch connects to what should be individual user PCs. Each port has the same port security configuration, configured as follows: interface range gigabitethernet 0/1 - 24 switchport mode access switchport port-security switchport port-security mac-address sticky Which of the following answers describe the result of the port security configuration created with these commands? (Choose two answers.)
Prevents unknown devices with unknown MAC addresses from sending data through the switch ports.
If a user connects a switch to the cable, prevents multiple devices from sending data through the port.
Will allow any one device to connect to each port and will save that device’s MAC address into the startup-config.
Will allow any one device to connect to each port but will not save that device’s MAC address into the startup-config.

## Slide 368
2. A Cisco Catalyst switch connects to what should be individual user PCs. Each port has the same port security configuration, configured as follows: interface range gigabitethernet 0/1 - 24 switchport mode access switchport port-security switchport port-security mac-address sticky Which of the following answers describe the result of the port security configuration created with these commands? (Choose two answers.)
Prevents unknown devices with unknown MAC addresses from sending data through the switch ports.
If a user connects a switch to the cable, prevents multiple devices from sending data through the port.
Will allow any one device to connect to each port and will save that device’s MAC address into the startup-config.
Will allow any one device to connect to each port but will not save that device’s MAC address into the startup-config.

## Slide 369
3. Which of the following commands list the MAC address table entries for MAC addresses configured by port security? (Choose two answers.)
show mac address-table dynamic
show mac address-table
show mac address-table static
show mac address-table port-security

## Slide 370
3. Which of the following commands list the MAC address table entries for MAC addresses configured by port security? (Choose two answers.)
show mac address-table dynamic
show mac address-table
show mac address-table static
show mac address-table port-security

## Slide 371
4. The show port-security interface f0/1 command lists a port status of secure-down. Which one of the following answers must be true about this interface at this time?
The show interface status command lists the interface status as connected.
The show interface status command lists the interface status as err-disabled.
The show port-security interface command could list a mode of shutdown or restrict, but not protect.
The show port-security interface command could list a violation counter value of 10.

## Slide 372
4. The show port-security interface f0/1 command lists a port status of secure-down. Which one of the following answers must be true about this interface at this time?
The show interface status command lists the interface status as connected.
The show interface status command lists the interface status as err-disabled.
The show port-security interface command could list a mode of shutdown or restrict, but not protect.
The show port-security interface command could list a violation counter value of 10.

## Slide 373
5. A switch’s port Gi0/1 has been correctly enabled with port security. The configuration sets the violation mode to restrict. A frame that violates the port security policy enters the interface, followed by a frame that does not. Which of the following answers correctly describe what happens in this scenario? (Choose two answers.)
The switch puts the interface into an err-disabled state when the first frame arrives.
The switch generates syslog messages about the violating traffic for the first frame.
The switch increments the violation counter for Gi0/1 by 1.
The switch discards both the first and second frame.

## Slide 374
5. A switch’s port Gi0/1 has been correctly enabled with port security. The configuration sets the violation mode to restrict. A frame that violates the port security policy enters the interface, followed by a frame that does not. Which of the following answers correctly describe what happens in this scenario? (Choose two answers.)
The switch puts the interface into an err-disabled state when the first frame arrives.
The switch generates syslog messages about the violating traffic for the first frame.
The switch increments the violation counter for Gi0/1 by 1.
The switch discards both the first and second frame.

## Slide 375
A PC connects to a LAN and uses DHCP to lease an IP address for the first time. Of the usual four DHCP messages that flow between the PC and the DHCP server, which ones do the client send? (Choose two answers.)
Acknowledgment
Discover
Offer
Request

## Slide 376
A PC connects to a LAN and uses DHCP to lease an IP address for the first time. Of the usual four DHCP messages that flow between the PC and the DHCP server, which ones do the client send? (Choose two answers.)
Acknowledgment
Discover
Offer
Request

## Slide 377
2. Which of the following kinds of information are part of a DHCP server configuration? (Choose two answers.)
Ranges of IP addresses in subnets that the server should lease
Ranges of IP addresses to not lease per subnet
DNS server hostnames
The default router IP and MAC address in each subnet

## Slide 378
2. Which of the following kinds of information are part of a DHCP server configuration? (Choose two answers.)
Ranges of IP addresses in subnets that the server should lease
Ranges of IP addresses to not lease per subnet
DNS server hostnames
The default router IP and MAC address in each subnet

## Slide 379
3. Which answers list a criterion for choosing which router interfaces need to be configured as a DHCP relay agent? (Choose two answers.)
If the subnet off the interface does not include a DHCP server
If the subnet off the interface does include a DHCP server
If the subnet off the interface contains DHCP clients
If the router interface already has an ip address dhcp command

## Slide 380
3. Which answers list a criterion for choosing which router interfaces need to be configured as a DHCP relay agent? (Choose two answers.)
If the subnet off the interface does not include a DHCP server
If the subnet off the interface does include a DHCP server
If the subnet off the interface contains DHCP clients
If the router interface already has an ip address dhcp command

## Slide 381
4. A router connects to an Internet Service Provider (ISP) using its G0/0/0 interface, with the ip address dhcp command configured. What does the router do with the DHCP learned default gateway information?
The router ignores the default gateway value learned from the DHCP server.
The router uses the default gateway just like a host, ignoring its routing table.
The router forwards received packets based on its routing table but uses its default gateway setting to forward packets it generates itself.
The router adds a default route based on the default gateway to its IP routing table.

## Slide 382
4. A router connects to an Internet Service Provider (ISP) using its G0/0/0 interface, with the ip address dhcp command configured. What does the router do with the DHCP learned default gateway information?
The router ignores the default gateway value learned from the DHCP server.
The router uses the default gateway just like a host, ignoring its routing table.
The router forwards received packets based on its routing table but uses its default gateway setting to forward packets it generates itself.
The router adds a default route based on the default gateway to its IP routing table.

## Slide 383
5. In the following excerpt from a command on a Mac, which of the following parts of the output represent information learned from a DHCP server? (Choose two answers.)
Macprompt$ ifconfig
en0 En1: flags=8863 mtu 1500 options=10b ether 00:6d:e7:b1:9a:11 inet 172.16.4.2 netmask 0xffffff00 broadcast 172.16.4.255
00:6d:e7:b1:9a:11
172.16.4.2
0xffffff00
172.16.4.255

## Slide 384
5. In the following excerpt from a command on a Mac, which of the following parts of the output represent information learned from a DHCP server? (Choose two answers.)
Macprompt$ ifconfig
en0 En1: flags=8863 mtu 1500 options=10b ether 00:6d:e7:b1:9a:11 inet 172.16.4.2 netmask 0xffffff00 broadcast 172.16.4.255
00:6d:e7:b1:9a:11
172.16.4.2
0xffffff00
172.16.4.255

## Slide 385
6. Which of the following commands on a Windows OS should list both the IP address and DNS servers as learned with DHCP?
ifconfig
ipconfig
ifconfig /all
ipconfig /all

## Slide 386
6. Which of the following commands on a Windows OS should list both the IP address and DNS servers as learned with DHCP?
ifconfig
ipconfig
ifconfig /all
ipconfig /all

## Slide 387
An engineer hears about DHCP Snooping and decides to implement it. Which of the following are the devices on which DHCP Snooping could be implemented? (Choose two answers.)
Layer 2 switches
Routers
Multilayer switches
End-user hosts

## Slide 388
An engineer hears about DHCP Snooping and decides to implement it. Which of the following are the devices on which DHCP Snooping could be implemented? (Choose two answers.)
Layer 2 switches
Routers
Multilayer switches
End-user hosts

## Slide 389
2. Layer 2 switch SW2 connects a Layer 2 switch (SW1), a router (R1), a DHCP server (S1), and three PCs (PC1, PC2, and PC3). All PCs are DHCP clients. Which of the following are the most likely DHCP Snooping trust state configurations on SW2 for the ports connected to the listed devices? (Choose two answers.)
The port connected to the router is untrusted.
The port connected to switch SW1 is trusted.
The port connected to PC1 is untrusted.
The port connected to PC3 is trusted.

## Slide 390
2. Layer 2 switch SW2 connects a Layer 2 switch (SW1), a router (R1), a DHCP server (S1), and three PCs (PC1, PC2, and PC3). All PCs are DHCP clients. Which of the following are the most likely DHCP Snooping trust state configurations on SW2 for the ports connected to the listed devices? (Choose two answers.)
The port connected to the router is untrusted.
The port connected to switch SW1 is trusted.
The port connected to PC1 is untrusted.
The port connected to PC3 is trusted.

## Slide 391
3. Switch SW1 needs to be configured to use DHCP Snooping in VLAN 5 and only VLAN 5. Which commands must be included, assuming at least one switch port in VLAN 5 must be an untrusted port? (Choose two answers.)
no ip dhcp snooping trust
ip dhcp snooping untrust
ip dhcp snooping
ip dhcp snooping vlan 5

## Slide 392
3. Switch SW1 needs to be configured to use DHCP Snooping in VLAN 5 and only VLAN 5. Which commands must be included, assuming at least one switch port in VLAN 5 must be an untrusted port? (Choose two answers.)
no ip dhcp snooping trust
ip dhcp snooping untrust
ip dhcp snooping
ip dhcp snooping vlan 5

## Slide 393
4. On a multilayer switch, a switch needs to be configured to perform DHCP Snooping on some Layer 2 ports in VLAN 3. Which command may or may not be needed depending on whether the switch also acts as a DHCP relay agent?
no ip dhcp snooping information option
ip dhcp snooping limit rate 5
errdisable recovery cause dhcp-rate-limit
ip dhcp snooping vlan 3

## Slide 394
4. On a multilayer switch, a switch needs to be configured to perform DHCP Snooping on some Layer 2 ports in VLAN 3. Which command may or may not be needed depending on whether the switch also acts as a DHCP relay agent?
no ip dhcp snooping information option
ip dhcp snooping limit rate 5
errdisable recovery cause dhcp-rate-limit
ip dhcp snooping vlan 3

## Slide 395
5. An ARP request arrives on port G0/1. Which answer describes two items DAI always compares regardless of the configuration?
The message’s ARP origin hardware address and the message’s Ethernet header source MAC address
The message’s ARP origin hardware address and the DHCP Snooping binding table
The message’s ARP target IP address and the DHCP Snooping binding table
The message’s ARP target IP address and the switch’s ARP table

## Slide 396
5. An ARP request arrives on port G0/1. Which answer describes two items DAI always compares regardless of the configuration?
The message’s ARP origin hardware address and the message’s Ethernet header source MAC address
The message’s ARP origin hardware address and the DHCP Snooping binding table
The message’s ARP target IP address and the DHCP Snooping binding table
The message’s ARP target IP address and the switch’s ARP table

## Slide 397
6. Switch SW1 needs to be configured to use Dynamic ARP Inspection along with DHCP Snooping in VLAN 6 and only VLAN 6. Which commands must be included, assuming at least one switch port in VLAN 6 must be a trusted port? (Choose two answers.)
no ip arp inspection untrust
ip arp inspection trust
ip arp inspection
ip arp inspection vlan 6

## Slide 398
6. Switch SW1 needs to be configured to use Dynamic ARP Inspection along with DHCP Snooping in VLAN 6 and only VLAN 6. Which commands must be included, assuming at least one switch port in VLAN 6 must be a trusted port? (Choose two answers.)
no ip arp inspection untrust
ip arp inspection trust
ip arp inspection
ip arp inspection vlan 6

## Slide 399
7. A Layer 2 switch needs to be configured to use Dynamic ARP Inspection along with DHCP Snooping. Which command would make DAI monitor ARP message rates on an interface at an average rate of 4 received ARP messages per second? (Choose two answers.)
ip arp inspection limit rate 4 burst interval 2
ip arp inspection limit rate 10 burst interval 2
ip arp inspection limit rate 16 burst interval 4
ip arp inspection limit rate 4

## Slide 400
7. A Layer 2 switch needs to be configured to use Dynamic ARP Inspection along with DHCP Snooping. Which command would make DAI monitor ARP message rates on an interface at an average rate of 4 received ARP messages per second? (Choose two answers.)
ip arp inspection limit rate 4 burst interval 2
ip arp inspection limit rate 10 burst interval 2
ip arp inspection limit rate 16 burst interval 4
ip arp inspection limit rate 4

## Slide 401
What level of logging to the console is the default for a Cisco device?
Informational
Errors
Warnings
Debugging

## Slide 402
What level of logging to the console is the default for a Cisco device?
Informational
Errors
Warnings
Debugging

## Slide 403
2. What command limits the messages sent to a syslog server to levels 4 through 0?
logging trap 0-4
logging trap 0,1,2,3,4
logging trap 4
logging trap through 4

## Slide 404
2. What command limits the messages sent to a syslog server to levels 4 through 0?
logging trap 0-4
logging trap 0,1,2,3,4
logging trap 4
logging trap through 4

## Slide 405
3. Which of the following is accurate about the NTP client function on a Cisco router?
The client synchronizes its time-of-day clock based on the NTP server.
It counts CPU cycles of the local router CPU to more accurately keep time.
The client synchronizes its serial line clock rate based on the NTP server.
The client must be connected to the same subnet as an NTP server.

## Slide 406
3. Which of the following is accurate about the NTP client function on a Cisco router?
The client synchronizes its time-of-day clock based on the NTP server.
It counts CPU cycles of the local router CPU to more accurately keep time.
The client synchronizes its serial line clock rate based on the NTP server.
The client must be connected to the same subnet as an NTP server.

## Slide 407
4. The only NTP configuration on router R1 is the ntp server 10.1.1.1 command. Which answers describe how NTP works on the router?
As an NTP server only
As an NTP client only
As an NTP server only after the NTP client synchronizes with NTP server 10.1.1.1
As an NTP server regardless of whether the NTP client synchronizes with NTP server 10.1.1.1

## Slide 408
4. The only NTP configuration on router R1 is the ntp server 10.1.1.1 command. Which answers describe how NTP works on the router?
As an NTP server only
As an NTP client only
As an NTP server only after the NTP client synchronizes with NTP server 10.1.1.1
As an NTP server regardless of whether the NTP client synchronizes with NTP server 10.1.1.1

## Slide 409
5. Imagine that a switch connects through an Ethernet cable to a router, and the router’s host name is Hannah. Which of the following commands could tell you information about the IOS version on Hannah without establishing a Telnet connection to Hannah? (Choose two answers.)
show neighbors Hannah
show cdp
show cdp neighbors
show cdp neighbors Hannah
show cdp entry Hannah
show cdp neighbors detail

## Slide 410
5. Imagine that a switch connects through an Ethernet cable to a router, and the router’s host name is Hannah. Which of the following commands could tell you information about the IOS version on Hannah without establishing a Telnet connection to Hannah? (Choose two answers.)
show neighbors Hannah
show cdp
show cdp neighbors
show cdp neighbors Hannah
show cdp entry Hannah
show cdp neighbors detail

## Slide 411
Which of the following summarized subnets represent routes that could have been created for CIDR’s goal to reduce the size of Internet routing tables?
10.0.0.0 255.255.255.0
10.1.0.0 255.255.0.0
200.1.1.0 255.255.255.0
200.1.0.0 255.255.0.0

## Slide 412
Which of the following summarized subnets represent routes that could have been created for CIDR’s goal to reduce the size of Internet routing tables?
10.0.0.0 255.255.255.0
10.1.0.0 255.255.0.0
200.1.1.0 255.255.255.0
200.1.0.0 255.255.0.0

## Slide 413
2. Which of the following are not private addresses according to RFC 1918? (Choose two answers.)
172.31.1.1
172.33.1.1
10.255.1.1
10.1.255.1
191.168.1.1

## Slide 414
2. Which of the following are not private addresses according to RFC 1918? (Choose two answers.)
172.31.1.1
172.33.1.1
10.255.1.1
10.1.255.1
191.168.1.1

## Slide 415
3. With static NAT, performing translation for inside addresses only, what causes NAT table entries to be created?
The first packet from the inside network to the outside network
The first packet from the outside network to the inside network
Configuration using the ip nat inside source command
Configuration using the ip nat outside source command

## Slide 416
3. With static NAT, performing translation for inside addresses only, what causes NAT table entries to be created?
The first packet from the inside network to the outside network
The first packet from the outside network to the inside network
Configuration using the ip nat inside source command
Configuration using the ip nat outside source command

## Slide 417
4. With dynamic NAT, performing translation for inside addresses only, what causes NAT table entries to be created?
The first packet from the inside network to the outside network
The first packet from the outside network to the inside network
Configuration using the ip nat inside source command
Configuration using the ip nat outside source command

## Slide 418
4. With dynamic NAT, performing translation for inside addresses only, what causes NAT table entries to be created?
The first packet from the inside network to the outside network
The first packet from the outside network to the inside network
Configuration using the ip nat inside source command
Configuration using the ip nat outside source command

## Slide 419
5. NAT has been configured to translate source addresses of packets for the inside part of the network, but only for some hosts as identified by an access control list. Which of the following commands indirectly identifies the hosts?
ip nat inside source list 1 pool barney
ip nat pool barney 200.1.1.1 200.1.1.254 netmask 255.255.255.0
ip nat inside
ip nat inside 200.1.1.1 200.1.1.2

## Slide 420
5. NAT has been configured to translate source addresses of packets for the inside part of the network, but only for some hosts as identified by an access control list. Which of the following commands indirectly identifies the hosts?
ip nat inside source list 1 pool barney
ip nat pool barney 200.1.1.1 200.1.1.254 netmask 255.255.255.0
ip nat inside
ip nat inside 200.1.1.1 200.1.1.2

## Slide 421
6. Examine the following configuration commands: interface Ethernet0/0 ip address 10.1.1.1 255.255.255.0 ip nat inside interface Serial0/0 ip address 200.1.1.249 255.255.255.252 ip nat inside source list 1 interface Serial0/0 access-list 1 permit 10.1.1.0 0.0.0.255 If the configuration is intended to enable source NAT overload, which of the following commands could be useful to complete the configuration? (Choose two answers.)
The ip nat outside command
The ip nat pat command
The overload keyword
The ip nat pool command

## Slide 422
6. Examine the following configuration commands: interface Ethernet0/0 ip address 10.1.1.1 255.255.255.0 ip nat inside interface Serial0/0 ip address 200.1.1.249 255.255.255.252 ip nat inside source list 1 interface Serial0/0 access-list 1 permit 10.1.1.0 0.0.0.255 If the configuration is intended to enable source NAT overload, which of the following commands could be useful to complete the configuration? (Choose two answers.)
The ip nat outside command
The ip nat pat command
The overload keyword
The ip nat pool command

## Slide 423
7. Examine the following show command output on a router configured for dynamic
NAT: -- Inside Source access-list 1 pool fred refcount 2288 pool fred: netmask 255.255.255.240 start 200.1.1.1 end 200.1.1.7 type generic, total addresses 7, allocated 7 (100%), misses 965
Users are complaining about not being able to reach the Internet. Which of the following is the most likely cause?
The problem is not related to NAT, based on the information in the command output.
The NAT pool does not have enough entries to satisfy all requests.
Standard ACL 1 cannot be used; an extended ACL must be used.
The command output does not supply enough information to identify the problem

## Slide 424
7. Examine the following show command output on a router configured for dynamic
NAT: -- Inside Source access-list 1 pool fred refcount 2288 pool fred: netmask 255.255.255.240 start 200.1.1.1 end 200.1.1.7 type generic, total addresses 7, allocated 7 (100%), misses 965
Users are complaining about not being able to reach the Internet. Which of the following is the most likely cause?
The problem is not related to NAT, based on the information in the command output.
The NAT pool does not have enough entries to satisfy all requests.
Standard ACL 1 cannot be used; an extended ACL must be used.
The command output does not supply enough information to identify the problem

## Slide 425
Which of the following attributes do QoS tools manage? (Choose three answers.)
Bandwidth
Delay
Load
MTU
Loss

## Slide 426
Which of the following attributes do QoS tools manage? (Choose three answers.)
Bandwidth
Delay
Load
MTU
Loss

## Slide 427
2. Which of the following QoS marking fields could remain with a packet while being sent through four different routers, over different LAN and WAN links? (Choose two answers.)
CoS
IPP
DSCP
MPLS EXP

## Slide 428
2. Which of the following QoS marking fields could remain with a packet while being sent through four different routers, over different LAN and WAN links? (Choose two answers.)
CoS
IPP
DSCP
MPLS EXP

## Slide 429
3. Which of the following are available methods of classifying packets in DiffServ on Cisco routers? (Choose three answers.)
Matching the IP DSCP field
Matching the 802.1p CoS field
Matching fields with an extended IP ACL
Matching the SNMP Location variable

## Slide 430
3. Which of the following are available methods of classifying packets in DiffServ on Cisco routers? (Choose three answers.)
Matching the IP DSCP field
Matching the 802.1p CoS field
Matching fields with an extended IP ACL
Matching the SNMP Location variable

## Slide 431
4. Which of the following behaviors are applied to a low latency queue in a Cisco router or switch? (Choose two answers.)
Shaping
Policing
Priority scheduling
Round-robin scheduling

## Slide 432
4. Which of the following behaviors are applied to a low latency queue in a Cisco router or switch? (Choose two answers.)
Shaping
Policing
Priority scheduling
Round-robin scheduling

## Slide 433
5. Think about a policing function that is currently working, and also think about a shaping function that is also currently working. That is, the current bit rate of traffic exceeds the respective policing and shaping rates. Which statements are true about these features? (Choose two answers.)
The policer may or may not be discarding packets.
The policer is definitely discarding packets.
The shaper may or may not be queuing packets to slow down the sending rate.
The shaper is definitely queuing packets to slow down the sending rate.

## Slide 434
5. Think about a policing function that is currently working, and also think about a shaping function that is also currently working. That is, the current bit rate of traffic exceeds the respective policing and shaping rates. Which statements are true about these features? (Choose two answers.)
The policer may or may not be discarding packets.
The policer is definitely discarding packets.
The shaper may or may not be queuing packets to slow down the sending rate.
The shaper is definitely queuing packets to slow down the sending rate.

## Slide 435
6. A queuing system has three queues serviced with round-robin scheduling and one low latency queue that holds all voice traffic. Round-robin queue 1 holds predominantly UDP traffic, while round-robin queues 2 and 3 hold predominantly TCP traffic. The packets in each queue happen to have a variety of DSCP markings per the QoS design. In which queues would it make sense to use a congestion avoidance (drop management) tool? (Choose two answers.)
The LLQ
Queue 1
Queue 2
Queue 3

## Slide 436
6. A queuing system has three queues serviced with round-robin scheduling and one low latency queue that holds all voice traffic. Round-robin queue 1 holds predominantly UDP traffic, while round-robin queues 2 and 3 hold predominantly TCP traffic. The packets in each queue happen to have a variety of DSCP markings per the QoS design. In which queues would it make sense to use a congestion avoidance (drop management) tool? (Choose two answers.)
The LLQ
Queue 1
Queue 2
Queue 3

## Slide 437
R1 and R2 attach to the same Ethernet VLAN, with subnet 10.1.19.0/25, with addresses 10.1.19.1 and 10.1.19.2, respectively, configured with the ip address interface subcommand. Host A refers to 10.1.19.1 as its default router, and host B refers to 10.1.19.2 as its default router. The routers do not use an FHRP. Which of the following is a problem for this LAN?
The design breaks IPv4 addressing rules because two routers cannot connect to the same LAN subnet.
If one router fails, neither host can send packets off-subnet.
If one router fails, both hosts will use the one remaining router as a default router.
If one router fails, the host that uses that router as a default router cannot send packets off-subnet.

## Slide 438
R1 and R2 attach to the same Ethernet VLAN, with subnet 10.1.19.0/25, with addresses 10.1.19.1 and 10.1.19.2, respectively, configured with the ip address interface subcommand. Host A refers to 10.1.19.1 as its default router, and host B refers to 10.1.19.2 as its default router. The routers do not use an FHRP. Which of the following is a problem for this LAN?
The design breaks IPv4 addressing rules because two routers cannot connect to the same LAN subnet.
If one router fails, neither host can send packets off-subnet.
If one router fails, both hosts will use the one remaining router as a default router.
If one router fails, the host that uses that router as a default router cannot send packets off-subnet.

## Slide 439
2. R1 and R2 attach to the same Ethernet VLAN, with subnet 10.1.19.0/25, with addresses 10.1.19.1 and 10.1.19.2, respectively, configured with the ip address interface subcommand. The routers use an FHRP. Host A and host B attach to the same LAN and have correct default router settings per the FHRP configuration. Which of the following statements is true for this LAN?
The design breaks IPv4 addressing rules because two routers cannot connect to the same LAN subnet.
If one router fails, neither host can send packets off-subnet.
If one router fails, both hosts will use the one remaining router as a default router.
If one router fails, only one of the two hosts will still be able to send packets off-subnet.

## Slide 440
2. R1 and R2 attach to the same Ethernet VLAN, with subnet 10.1.19.0/25, with addresses 10.1.19.1 and 10.1.19.2, respectively, configured with the ip address interface subcommand. The routers use an FHRP. Host A and host B attach to the same LAN and have correct default router settings per the FHRP configuration. Which of the following statements is true for this LAN?
The design breaks IPv4 addressing rules because two routers cannot connect to the same LAN subnet.
If one router fails, neither host can send packets off-subnet.
If one router fails, both hosts will use the one remaining router as a default router.
If one router fails, only one of the two hosts will still be able to send packets off-subnet.

## Slide 441
3. R1 and R2 attach to the same Ethernet VLAN, with subnet 10.1.19.0/25, with addresses 10.1.19.1 and 10.1.19.2, respectively, configured with the ip address interface subcommand. The routers use HSRP. The network engineer prefers to have R1 be the default router when both R1 and R2 are up. Which of the following is the likely default router setting for hosts in this subnet?
10.1.19.1
10.1.19.2
Another IP address in subnet 10.1.19.0/25 other than 10.1.19.1 and 10.1.19.2
A host name that the FHRP mini-DNS will initially point to 10.1.19.1

## Slide 442
3. R1 and R2 attach to the same Ethernet VLAN, with subnet 10.1.19.0/25, with addresses 10.1.19.1 and 10.1.19.2, respectively, configured with the ip address interface subcommand. The routers use HSRP. The network engineer prefers to have R1 be the default router when both R1 and R2 are up. Which of the following is the likely default router setting for hosts in this subnet?
10.1.19.1
10.1.19.2
Another IP address in subnet 10.1.19.0/25 other than 10.1.19.1 and 10.1.19.2
A host name that the FHRP mini-DNS will initially point to 10.1.19.1

## Slide 443
4. A Network Management Station (NMS) is using SNMP to manage some Cisco routers and switches with SNMPv2c. Which of the following answers most accurately describes how the SNMP agent on a router authenticates any SNMP Get requests received from the NMS?
Using a username and hashed version of a password
Using either the read-write or read-only community string
Using only the read-write community string
Using only the read-only community string

## Slide 444
4. A Network Management Station (NMS) is using SNMP to manage some Cisco routers and switches with SNMPv2c. Which of the following answers most accurately describes how the SNMP agent on a router authenticates any SNMP Get requests received from the NMS?
Using a username and hashed version of a password
Using either the read-write or read-only community string
Using only the read-write community string
Using only the read-only community string

## Slide 445
5. Which of the following SNMP messages are typically sent by an SNMP agent? (choose two)
Trap
Get Request
Inform
Set Request

## Slide 446
5. Which of the following SNMP messages are typically sent by an SNMP agent?(Choose two)
Trap
Get Request
Inform
Set Request

## Slide 447
6. An FTP client connects to an FTP server using active mode and retrieves a copy of a file from the server. Which of the answers describes a TCP connection initiated by the FTP client?
The FTP control connection
The FTP data connection
The FTP TLS connection
None of the other answers are correct.

## Slide 448
6. An FTP client connects to an FTP server using active mode and retrieves a copy of a file from the server. Which of the answers describes a TCP connection initiated by the FTP client?
The FTP control connection
The FTP data connection
The FTP TLS connection
None of the other answers are correct.

## Slide 449
7. Which of the following functions are supported by FTP but not by TFTP? (Choose two answers.)
a. Transferring files from client to server
b. Changing the current directory on the server
c. Transferring files from server to client
d. Listing directory contents of a server’s directory

## Slide 450
7. Which of the following functions are supported by FTP but not by TFTP? (Choose two answers.)
a. Transferring files from client to server
b. Changing the current directory on the server
c. Transferring files from server to client
d. Listing directory contents of a server’s directory

## Slide 451
In a two-tier campus LAN design, which of the following are typically true of the topology design? (Choose two answers.)
The design uses a full mesh of links between access and distribution switches.
The design uses a partial mesh of links between access and distribution switches.
The design uses a partial mesh of links between the distribution and core switches.
The end-user and server devices connect directly to access layer switches.

## Slide 452
In a two-tier campus LAN design, which of the following are typically true of the topology design? (Choose two answers.)
The design uses a full mesh of links between access and distribution switches.
The design uses a partial mesh of links between access and distribution switches.
The design uses a partial mesh of links between the distribution and core switches.
The end-user and server devices connect directly to access layer switches.

## Slide 453
2. In a three-tier campus LAN design, which of the following are typically true of the topology design? (Choose two answers.)
The design uses a partial mesh of links between access and distribution switches.
The design uses a full mesh of links between access and distribution switches.
The design uses a partial mesh of links between the distribution and core switches.
The end-user and server devices connect directly to distribution layer switches.

## Slide 454
2. In a three-tier campus LAN design, which of the following are typically true of the topology design? (Choose two answers.)
The design uses a partial mesh of links between access and distribution switches.
The design uses a full mesh of links between access and distribution switches.
The design uses a partial mesh of links between the distribution and core switches.
The end-user and server devices connect directly to distribution layer switches.

## Slide 455
3. Which one answer gives the strongest match between one part of a typical three-tier design with the idea behind the listed generic topology design term?
The access layer looks like a partial mesh.
The distribution layer looks like a full mesh.
The distribution layer looks like a hybrid design.
The access layer looks like a star design.

## Slide 456
3. Which one answer gives the strongest match between one part of a typical three-tier design with the idea behind the listed generic topology design term?
The access layer looks like a partial mesh.
The distribution layer looks like a full mesh.
The distribution layer looks like a hybrid design.
The access layer looks like a star design.

## Slide 457
4. Which answers list criteria typical of a SOHO network? (Choose two answers.)
The AP functions using standalone mode.
The AP functions using a split-MAC architecture using a WLC.
A single networking device implements the router, switch, AP, and firewall functions.
A separate networking device implements each function (router, switch, AP, and firewall).

## Slide 458
4. Which answers list criteria typical of a SOHO network? (Choose two answers.)
The AP functions using standalone mode.
The AP functions using a split-MAC architecture using a WLC.
A single networking device implements the router, switch, AP, and firewall functions.
A separate networking device implements each function (router, switch, AP, and firewall).

## Slide 459
5. Which answer describes how a LAN switch dynamically chooses the initial power level to apply to a UTP cable with PoE?
Autonegotiation
CDP
LLDP
Preconfigured values

## Slide 460
5. Which answer describes how a LAN switch dynamically chooses the initial power level to apply to a UTP cable with PoE?
Autonegotiation
CDP
LLDP
Preconfigured values

## Slide 461
6. Which of the following refer to standards that deliver power over all four pairs in a UTP cable? (Choose two answers.)
PoE
UPoE
PoE+
UPoE+

## Slide 462
6. Which of the following refer to standards that deliver power over all four pairs in a UTP cable? (Choose two answers.)
PoE
UPoE
PoE+
UPoE+

## Slide 463
Which of the following topology terms most closely describe the topology created by a Metro Ethernet Tree (E-Tree) service? (Choose two answers.)
Full mesh
Partial mesh
Hub and spoke
Point-to-point

## Slide 464
Which of the following topology terms most closely describe the topology created by a Metro Ethernet Tree (E-Tree) service? (Choose two answers.)
Full mesh
Partial mesh
Hub and spoke
Point-to-point

## Slide 465
2. Which of the following is the most likely technology used for an access link to a Metro Ethernet service?
100BASE-LX10
High-speed TDM (for example, T3, E3)
MPLS
100BASE-T

## Slide 466
2. Which of the following is the most likely technology used for an access link to a Metro Ethernet service?
100BASE-LX10
High-speed TDM (for example, T3, E3)
MPLS
100BASE-T

## Slide 467
3. An enterprise uses a Metro Ethernet WAN with an Ethernet LAN (E-LAN) service, with the company headquarters plus 10 remote sites connected to the service. The enterprise uses OSPF at all sites, with one router connected to the service from each site. Which of the following are true about the Layer 3 details most likely used with this service and design? (Choose two answers.)
The WAN uses one IP subnet.
The WAN uses 10 or more IP subnets.
A remote site router would have one OSPF neighbor.
A remote site router would have 10 OSPF neighbors.

## Slide 468
3. An enterprise uses a Metro Ethernet WAN with an Ethernet LAN (E-LAN) service, with the company headquarters plus 10 remote sites connected to the service. The enterprise uses OSPF at all sites, with one router connected to the service from each site. Which of the following are true about the Layer 3 details most likely used with this service and design? (Choose two answers.)
The WAN uses one IP subnet.
The WAN uses 10 or more IP subnets.
A remote site router would have one OSPF neighbor.
A remote site router would have 10 OSPF neighbors.

## Slide 469
4. An enterprise uses an MPLS Layer 3 VPN with the company headquarters connected plus 10 remote sites connected to the service. The enterprise uses OSPF at all sites, with one router connected to the service from each site. Which of the following are true about the Layer 3 details most likely used with this service and design? (Choose two answers.)
The WAN uses one IP subnet.
The WAN uses 10 or more IP subnets.
A remote site router would have one OSPF neighbor.
A remote site router would have 10 or more OSPF neighbors.

## Slide 470
4. An enterprise uses an MPLS Layer 3 VPN with the company headquarters connected plus 10 remote sites connected to the service. The enterprise uses OSPF at all sites, with one router connected to the service from each site. Which of the following are true about the Layer 3 details most likely used with this service and design? (Choose two answers.)
The WAN uses one IP subnet.
The WAN uses 10 or more IP subnets.
A remote site router would have one OSPF neighbor.
A remote site router would have 10 or more OSPF neighbors.

## Slide 471
5. Which of the following answers is most accurate about access link options for an MPLS network?
Uses only TDM (T1, T3, E1, E3, etc.)
Uses only Ethernet
Uses only DSL and cable
Uses a wide variety of Layer 1 and Layer 2 networking technologies

## Slide 472
5. Which of the following answers is most accurate about access link options for an MPLS network?
Uses only TDM (T1, T3, E1, E3, etc.)
Uses only Ethernet
Uses only DSL and cable
Uses a wide variety of Layer 1 and Layer 2 networking technologies

## Slide 473
6. An enterprise connects 20 sites into an MPLS VPN WAN. The enterprise uses OSPF for IPv4 routes at all sites. Consider the OSPF area design options and the PE-CE links. Which of the following answers is most accurate about OSPF areas and the PE-CE links?
The PE-CE link may or may not be chosen to be in backbone area 0.
b. The PE-CE link must not be in the backbone area 0.
c. The PE-CE link must be in the backbone area 0.
d. The PE-CE link will not be in any OSPF area.

## Slide 474
6. An enterprise connects 20 sites into an MPLS VPN WAN. The enterprise uses OSPF for IPv4 routes at all sites. Consider the OSPF area design options and the PE-CE links. Which of the following answers is most accurate about OSPF areas and the PE-CE links?
The PE-CE link may or may not be chosen to be in backbone area 0.
b. The PE-CE link must not be in the backbone area 0.
c. The PE-CE link must be in the backbone area 0.
d. The PE-CE link will not be in any OSPF area.

## Slide 475
7. A colleague mentions using a remote access VPN. Which of the following protocols or technologies would you expect your colleague to have used?
TLS
IPsec
GRE
FTPS

## Slide 476
7. A colleague mentions using a remote access VPN. Which of the following protocols or technologies would you expect your colleague to have used?
TLS
IPsec
GRE
FTPS

## Slide 477
Three virtual machines run on one physical server. Which of the following server resources are commonly virtualized so each VM can use the required amount of that resource? (Choose three answers.)
NIC
RAM
Power
Hypervisor
CPU

## Slide 478
Three virtual machines run on one physical server. Which of the following server resources are commonly virtualized so each VM can use the required amount of that resource? (Choose three answers.)
NIC
RAM
Power
Hypervisor
CPU

## Slide 479
2. Eight virtual machines run on one physical server; the server has two physical Ethernet NICs. Which answer describes a method that allows all eight VMs to communicate?
The VMs must share two IP addresses and coordinate to avoid using duplicate TCP or UDP ports.
The hypervisor acts as an IP router using the NICs as routed IP interfaces.
Each VM uses a virtual NIC that is mapped to a physical NIC.
Each VM uses a virtual NIC that logically connects to a virtual switch.

## Slide 480
2. Eight virtual machines run on one physical server; the server has two physical Ethernet NICs. Which answer describes a method that allows all eight VMs to communicate?
The VMs must share two IP addresses and coordinate to avoid using duplicate TCP or UDP ports.
The hypervisor acts as an IP router using the NICs as routed IP interfaces.
Each VM uses a virtual NIC that is mapped to a physical NIC.
Each VM uses a virtual NIC that logically connects to a virtual switch.

## Slide 481
3. Which of the following cloud services is most likely to be used for software development?
IaaS
PaaS
SaaS
SLBaaS

## Slide 482
3. Which of the following cloud services is most likely to be used for software development?
IaaS
PaaS
SaaS
SLBaaS

## Slide 483
4. Which of the following cloud services is most likely to be purchased and then used to later install your own software applications?
IaaS
PaaS
SaaS
SLBaaS

## Slide 484
4. Which of the following cloud services is most likely to be purchased and then used to later install your own software applications?
IaaS
PaaS
SaaS
SLBaaS

## Slide 485
5. An enterprise plans to start using a public cloud service and is considering different WAN options. The answers list four options under consideration. Which one option has the most issues if the company chooses one cloud provider but then later wants to change to use a different cloud provider instead?
Using private WAN connections directly to the cloud provider
Using an Internet connection without VPN
Using an intercloud exchange
Using an Internet connection with VPN

## Slide 486
5. An enterprise plans to start using a public cloud service and is considering different WAN options. The answers list four options under consideration. Which one option has the most issues if the company chooses one cloud provider but then later wants to change to use a different cloud provider instead?
Using private WAN connections directly to the cloud provider
Using an Internet connection without VPN
Using an intercloud exchange
Using an Internet connection with VPN

## Slide 487
6. An enterprise plans to start using a public cloud service and is considering different WAN options. The answers list four options under consideration. Which options provide good security by keeping the data private while also providing good QoS services? (Choose two answers.)
Using private WAN connections directly to the cloud provider
Using an Internet connection without VPN
Using an intercloud exchange
Using an Internet connection with VPN

## Slide 488
6. An enterprise plans to start using a public cloud service and is considering different WAN options. The answers list four options under consideration. Which options provide good security by keeping the data private while also providing good QoS services? (Choose two answers.)
Using private WAN connections directly to the cloud provider
Using an Internet connection without VPN
Using an intercloud exchange
Using an Internet connection with VPN

## Slide 489
A Layer 2 switch examines a frame’s destination MAC address and chooses to forward that frame out port G0/1 only. That action occurs as part of which plane of the switch?
Data plane
Management plane
Control plane
Table plane

## Slide 490
A Layer 2 switch examines a frame’s destination MAC address and chooses to forward that frame out port G0/1 only. That action occurs as part of which plane of the switch?
Data plane
Management plane
Control plane
Table plane

## Slide 491
2. A router uses OSPF to learn routes and adds those to the IPv4 routing table. That action occurs as part of which plane of the switch?
Data plane
Management plane
Control plane
Table plane

## Slide 492
2. A router uses OSPF to learn routes and adds those to the IPv4 routing table. That action occurs as part of which plane of the switch?
Data plane
Management plane
Control plane
Table plane

## Slide 493
3. A network uses an SDN architecture with switches and a centralized controller. Which of the following terms describes a function or functions expected to be found on the switches but not on the controller?
A northbound interface
A southbound interface
Data plane functions
Control plane functions

## Slide 494
3. A network uses an SDN architecture with switches and a centralized controller. Which of the following terms describes a function or functions expected to be found on the switches but not on the controller?
A northbound interface
A southbound interface
Data plane functions
Control plane functions

## Slide 495
4. Which of the following controllers (if any) uses a mostly centralized control plane model?
OpenDaylight Controller
Cisco Application Policy Infrastructure Controller (APIC)
Cisco APIC Enterprise Module (APIC-EM)
None of these controllers uses a mostly centralized control plane.

## Slide 496
4. Which of the following controllers (if any) uses a mostly centralized control plane model?
OpenDaylight Controller
Cisco Application Policy Infrastructure Controller (APIC)
Cisco APIC Enterprise Module (APIC-EM)
None of these controllers uses a mostly centralized control plane.

## Slide 497
5. To which types of nodes should an ACI leaf switch connect in a typical single-site design? (Choose two answers.)
All of the other leaf switches
A subset of the spine switches
All of the spine switches
Some of the endpoints
None of the endpoints

## Slide 498
5. To which types of nodes should an ACI leaf switch connect in a typical single-site design? (Choose two answers.)
All of the other leaf switches
A subset of the spine switches
All of the spine switches
Some of the endpoints
None of the endpoints

## Slide 499
Which answers list an advantage of controller-based networks versus traditional networks? (Choose two answers.)
The ability to configure the features for the network rather than per device
The ability to have forwarding tables at each device
Programmatic APIs available per device
More consistent device configuration

## Slide 500
Which answers list an advantage of controller-based networks versus traditional networks? (Choose two answers.)
The ability to configure the features for the network rather than per device
The ability to have forwarding tables at each device
Programmatic APIs available per device
More consistent device configuration

## Slide 501
In Cisco Software-Defined Access (SDA), which term refers to the devices and cabling, along with configuration that allows the network device nodes enough IP connectivity to send IP packets to each other?
Fabric
Overlay
Underlay
VXLAN

## Slide 502
In Cisco Software-Defined Access (SDA), which term refers to the devices and cabling, along with configuration that allows the network device nodes enough IP connectivity to send IP packets to each other?
Fabric
Overlay
Underlay
VXLAN

## Slide 503
2. In Cisco Software-Defined Access (SDA), which term refers to the functions that deliver endpoint packets across the network using tunnels between the ingress and egress fabric nodes?
Fabric
Overlay
Underlay
VXLAN

## Slide 504
2. In Cisco Software-Defined Access (SDA), which term refers to the functions that deliver endpoint packets across the network using tunnels between the ingress and egress fabric nodes?
Fabric
Overlay
Underlay
VXLAN

## Slide 505
3. In Software-Defined Access (SDA), which of the answers are part of the overlay data plane?
LISP
GRE
OSPF
VXLAN

## Slide 506
3. In Software-Defined Access (SDA), which of the answers are part of the overlay data plane?
LISP
GRE
OSPF
VXLAN

## Slide 507
Which answers best describe options of how to implement security with scalable groups using DNA Center and SDA? (Choose two answers.)
A human user from the DNA Center GUI
An automation application using NETCONF
A human user using the CLI of an SDA fabric edge node
An automation application using REST

## Slide 508
Which answers best describe options of how to implement security with scalable groups using DNA Center and SDA? (Choose two answers.)
A human user from the DNA Center GUI
An automation application using NETCONF
A human user using the CLI of an SDA fabric edge node
An automation application using REST

## Slide 509
5. Which of the following protocols or tools could be used as part of the Cisco DNA Center southbound interface? (Choose three answers.)
Ansible
SSH
NETCONF
SNMP
Puppet

## Slide 510
5. Which of the following protocols or tools could be used as part of the Cisco DNA Center southbound interface? (Choose three answers.)
Ansible
SSH
NETCONF
SNMP
Puppet

## Slide 511
6. Which of the following are network management features performed by both traditional network management software as well as by DNA Center? (Choose two answers.)
Network device discovery
Software-Defined Access configuration
End-to-end path discovery with ACL analysis
Device installation (day 0), configuration (day 1), and monitoring (day n) operations

## Slide 512
6. Which of the following are network management features performed by both traditional network management software as well as by DNA Center? (Choose two answers.)
Network device discovery
Software-Defined Access configuration
End-to-end path discovery with ACL analysis
Device installation (day 0), configuration (day 1), and monitoring (day n) operations

## Slide 513
Which of the following are required attributes of a REST-based API? (Choose two answers.)
Uses HTTP
Objects noted as to whether they can be cached
Classful operation
Client/server architecture

## Slide 514
Which of the following are required attributes of a REST-based API? (Choose two answers.)
Uses HTTP
Objects noted as to whether they can be cached
Classful operation
Client/server architecture

## Slide 515
Which answers list a matching software development CRUD action to an HTTP verb that performs that action? (Choose two answers.)
CRUD create and HTTP PATCH
CRUD update and HTTP PATCH
CRUD delete and HTTP PUT
CRUD read and HTTP GET

## Slide 516
Which answers list a matching software development CRUD action to an HTTP verb that performs that action? (Choose two answers.)
CRUD create and HTTP PATCH
CRUD update and HTTP PATCH
CRUD delete and HTTP PUT
CRUD read and HTTP GET

## Slide 517
3. Examine the following URI that works with a Cisco DNA Controller: https://dnac.example.com/dna/intent/api/v1/network-device?managementIPAddress=10.10.22.74 Which part of the URI, per the API documentation, is considered to identify the resource but not any parameters?
https://
dnac.example.com
dna/intent/api/v1/network-device
managementIPAddress=10.10.22.74

## Slide 518
3. Examine the following URI that works with a Cisco DNA Controller: https://dnac.example.com/dna/intent/api/v1/network-device?managementIPAddress=10.10.22.74 Which part of the URI, per the API documentation, is considered to identify the resource but not any parameters?
https://
dnac.example.com
dna/intent/api/v1/network-device
managementIPAddress=10.10.22.74

## Slide 519
4. Which of the following data serialization and data modeling languages would be most likely to be used in a response from a REST-based server API used for networking applications? (Choose two answers.)
JSON
YAML
JavaScript
XML

## Slide 520
4. Which of the following data serialization and data modeling languages would be most likely to be used in a response from a REST-based server API used for networking applications? (Choose two answers.)
JSON
YAML
JavaScript
XML

## Slide 521
5. Which answers correctly describe the format of the JSON text below? (Choose two answers.) { "myvariable":[1,2,3] }
One JSON object that has one key:value pair
One JSON object that has three key:value pairs
A JSON object whose value is a second JSON object
A JSON object whose value is a JSON array

## Slide 522
5. Which answers correctly describe the format of the JSON text below? (Choose two answers.) { "myvariable":[1,2,3] }
One JSON object that has one key:value pair
One JSON object that has three key:value pairs
A JSON object whose value is a second JSON object
A JSON object whose value is a JSON array

## Slide 523
Which answer best describes the meaning of the term configuration drift?
Changes to a single device’s configuration over time versus that single device’s original configuration
Larger and larger sections of unnecessary configuration in a device
Changes to a single device’s configuration over time versus other devices that have the same role
Differences in device configuration versus a centralized backup copy

## Slide 524
Which answer best describes the meaning of the term configuration drift?
Changes to a single device’s configuration over time versus that single device’s original configuration
Larger and larger sections of unnecessary configuration in a device
Changes to a single device’s configuration over time versus other devices that have the same role
Differences in device configuration versus a centralized backup copy

## Slide 525
2. An enterprise moves away from manual configuration methods, making changes by editing centralized configuration files. Which answers list an issue solved by using a version control system with those centralized files? (Choose two answers.)
The ability to find which engineer changed the central configuration file on a date/time
The ability to find the details of what changed in the configuration file over time
The ability to use a template with per-device variables to create configurations
The ability to recognize configuration drift in a device and notify the staff

## Slide 526
2. An enterprise moves away from manual configuration methods, making changes by editing centralized configuration files. Which answers list an issue solved by using a version control system with those centralized files? (Choose two answers.)
The ability to find which engineer changed the central configuration file on a date/time
The ability to find the details of what changed in the configuration file over time
The ability to use a template with per-device variables to create configurations
The ability to recognize configuration drift in a device and notify the staff

## Slide 527
3. Configuration monitoring (also called configuration enforcement) by a configuration management tool generally solves which problem?
Tracking the identity of individuals who changed files, along with which files they changed
Listing differences between a former and current configuration
Testing a configuration change to determine whether it will be rejected or not when implemented
Finding instances of configuration drift

## Slide 528
3. Configuration monitoring (also called configuration enforcement) by a configuration management tool generally solves which problem?
Tracking the identity of individuals who changed files, along with which files they changed
Listing differences between a former and current configuration
Testing a configuration change to determine whether it will be rejected or not when implemented
Finding instances of configuration drift

## Slide 529
4. Which of the following configuration management tools uses a push model to configure network devices?
Ansible
Puppet
Chef
None use a push model

## Slide 530
4. Which of the following configuration management tools uses a push model to configure network devices?
Ansible
Puppet
Chef
None use a push model

## Slide 531
5. Which of the following answers list a correct combination of configuration management tool and the term used for one of its primary configuration files? (Choose two answers.)
Ansible manifest
Puppet manifest
Chef recipe
Ansible recipe

## Slide 532
5. Which of the following answers list a correct combination of configuration management tool and the term used for one of its primary configuration files? (Choose two answers.)
Ansible manifest
Puppet manifest
Chef recipe
Ansible recipe